## Slide 1
VECTO 3.x
16.3.2023
Release Notes

## Slide 2: Vecto 0.7.10.2996 Development Version March 2023
Important Note This is a development release for xEV-Lorries. Bus related functionalities may be broken.
Changes
  Implementation of Declaration-Mode for xEV-Lorries
    Support for xEV-JSON-Jobs in Declaration Mode
    New generic vehicles (XML & JSON)
  Test settings:
    Charge-Sustaining-Mode:
      Iterative simulation for OVC-P-HEVs
      can be disabled
    Charge-Depleting-Mode:
      Central SOC can be overridden for
      Charge-Depleting-Mode
  Declaration values can be overridden by copying the particular file to <VectoDir>\Declaration\Override and changing the desired value.
  New XSD-Schema for XML Reports
  Updated Hybrid Strategy and Gearshifting

## Slide 3: Declaration Mode Lorries – Overview (1/2)
VECTO Development Version 0.7.10.2996 as released on March 15, features the Declaration Mode for Lorries according to the 2nd Amendment.
This enables the official output XMLs (MRF, CIF) to be generated using the official input XMLs.
The result values correspond to the official results, subject to minor adjustments and additions from the testing period (see later slides).
With this version, the Declaration Mode can also be calculated via the GUI (json + csv). This mode also contains some special features for the upcoming test phase (see later slides).

## Slide 4: Declaration Mode Lorries – Overview (2/2)
Overview new elements
  Generic parameterisation of auxiliaries
  Generic parametrisation of P-HEV strategy including update of gear shift strategy
  Generic parametrisation of S-HEV strategy
  Generic parametrisation of usable SOC range
  Separate approach for „Charge depleting mode“ simulation
  Calculation of energy consumption at “battery terminals” considering battery charging losses during external charging
  Range calculations
  Automation of the various simulation runs necessary for PHEVs plus post processing elements
  Generic e-PTO cycle for PEV and S-HEV in the MUN cycle
  Generation of MRF and CIF

## Slide 5: DECL Lorries – Generic parameterisation of auxiliaries
Basic principles of generic data used in DECL
  Relevant auxiliary systems:
    Pneumatic system
    ICE cooling fan + conditioning power for electric propulsion components
    Steering system
    HVAC: for lorries only “yes/no”
    Electric board net (is called “electric system”): for lorries only headlights technology (LED or standard)
  Respective tables with generic power demand for each auxiliary system can be found in specific subfolder “Declaration\VAUX” under VECTO main path as csv-files
  General table structure looks as follows:
Technology | conventional | P-HEV | S-HEV | PEV | fully electric | Long haul | Regional delivery | Urban delivery | Municipal utility | Construction
Tech #1 |  |  |  |  |  |  |  |  |  | 
Tech #2 |  |  |  |  |  |  |  |  |  | 
Tech #3 |  |  |  |  |  |  |  |  |  | 
Tech #... |  |  |  |  |  |  |  |  |  | 
can be directly supplied by REESS if present (indicated with 0/1)
cycle specific mechanical power demand [W]
applicability for architecture (indicated with 0/1)

## Slide 6: DECL Lorries – Generic parameterisation of auxiliaries
Basic principles of generic data used in DECL
  Details of application in DECL:
    For all HEV: "fully electric" technology is connected to REESS  mechanical power (i.e. respective alternator drive power) is converted to electric power with generic alternator efficiency of 0.7 used consistently throughout whole VECTO auxiliary approach (i.e. mechanical power from table is multiplied by 0.7 and therefore reduced)
    For all PEV: only "fully electric" technology can be declared (acc. to Annex specifications as well)  same principle of conversion from mechanical to electrical power (as explained above applies)
Technology | conventional | P-HEV | S-HEV | PEV | fully electric | Long haul | Regional delivery | Urban delivery | Municipal utility | Construction
Tech #1 |  |  |  |  |  |  |  |  |  | 
Tech #2 |  |  |  |  |  |  |  |  |  | 
Tech #3 |  |  |  |  |  |  |  |  |  | 
Tech #... |  |  |  |  |  |  |  |  |  | 
can be directly supplied by REESS if present (indicated with 0/1)
cycle specific mechanical power demand [W]
applicability for architecture (indicated with 0/1)

## Slide 7: DECL Lorries – Generic parameterisation of auxiliaries
Block of mechanical technologies
Basic principles of pneumatic system in DECL
  Structure of table is slightly different, stating mechanical and electrical power demand at the same time
  Reason is that generic saving of AMS techonolgies is reduced for xEV vehicles (only minus 10%) due to reduced recuperative potential compared to conventional ones
Technology | conventional | P-HEV | S-HEV | PEV | fully electric | mechanical power demand [W] | electrical power demand [W]
Tech mechanical #1 |  |  |  |  |  |  | 
Tech mechanical #2 |  |  |  |  |  |  | 
Tech mechanical #3 |  |  |  |  |  |  | 
Tech mechanical #... |  |  |  |  |  |  | 
Tech electrical #1 |  |  |  |  |  |  | 
Tech electrical #2 |  |  |  |  |  |  | 
Tech electrical #3 |  |  |  |  |  |  | 
Tech electrical #... |  |  |  |  |  |  | 
can be directly supplied by REESS if present (indicated with 0/1)
applicability for architecture (indicated with 0/1)
Block of electrical technologies
cycle specific indication of power demand [W]
PS-Table.csv

## Slide 8: DECL Lorries – Generic parameterisation of auxiliaries
Basic principles of ICE fan and electric components conditioning power in DECL
  ICE fan power is always fully applied when ICE = on in simulation
  For PEV and S-HEV: values from table below are fully applied when at least one EM = on in simulation (i.e. electric powertrain is propelling/braking) or when E_PTO = on
  For P-HEV: values from table below are applied according to equations further below with scaling factor “x” reflecting actual split of propulsion power for each timestep
    x = ABS(PEM) / [ABS(PEM) + ABS(PICE)] with and PEM and PICE being the mechanical power of EM and ICE
    Applied electric components conditioning power equals: “table value” multiplied by x
    For further details please refer to VECTO-DEV WS#12 18.05.2022 (slide 15ff)
Electric conditioning power demand applied to electric system [W] |  |  |  | 
Long Haul | Regional Delivery | Urban Delivery | Municipal utility | Construction
600 | 600 | 550 | 550 | 600
Fan-Tech.csv + Cond-Table.csv

## Slide 9: DECL Lorries – Generic parameterisation of auxiliaries
Basic principles of steering system in DECL
  Foundation of approach is that basic power demand defined per cycle is multiplied by technology dependent scaling factors (CFs)
  3 sub-groups of power demands defined:
    U&F: unloaded and friction
    B: banking
    S: steering
  Total steering power acc. to equation below is calculated separately for mechanical and electrical stering power demand:
    All CFs are averaged over all steered axles with electric technology
    All CFs are averaged over all steered axles with mechanical technology
  If all axles are electric technologies, total steering power is applied as electrical power to REESS
  With at least one mechanical techn. present, total steering power is applied as mechanical load
SP-Tech.csv + SP-Table.csv + SP-Axles.csv

## Slide 10: DECL Lorries – Generic parameterisation of auxiliaries
Basic principles of HVAC system in DECL
  Conventional and P-HEV:
    HVAC load is applied as mechanical auxiliary
  S-HEV and PEV:
    HVAC load is applied as electrical auxiliary
    Conversion from mechanical to electrical is done by dividing mechanical base power by generic efficiency of 0.8
HVAC-Table.csv

## Slide 11: DECL Lorries – Generic parameterisation of auxiliaries
General remark about post-processing of “missing” auxiliary power demand for mechanically driven auxiliaries in timesteps where the ICE is off:
  These topic is related to “Utility Factor (UF) for Engine-Stop-Start (ESS)”
  For lorries only the very simple case is relevant (application case 1)
  Basic rule: for auxiliaries operated independently of ICE status energy demand over cycle is the same with missing portion being accounted for in post-processing
  For further details please refer to: VECTO-DEV WS#6 12.07.2021 (slide 7ff)

## Slide 12: DECL Lorries – Generic parametrisation P-HEV strategy
Operation in Charge sustaining (CS) mode
  Fixed number of 3 simulations to determine optimal strategy parameters done automatically
  1st run: generic start value for equivalence factor (EF) depending on vehicle group, mission, payload and usable SOC range applied
    refer to \Declaration\HEVParameters\Lorry\HEV_Strategy_Parameters_fequiv_XXsoc.csv
    XX = 10, 20 or 40 depending on usable SOC range in percent (interpolation, no extrapolation)
  2nd run: from resulting ∆SOC1 of 1st run (∆SOC = SOCEnd – SOCStart) new EF is calculated according to following equations:
  3rd run: from resulting ∆SOC2 of 2nd run new equivalence factor is calculated according to following equation:
  For further details please refer to: VECTO-DEV WS#8 16.11.2021 (slide 7ff)
with
equivalence factor used in 1st simulation run
refer to \Declaration\HEVParameters\Lorry\Gradient_40.csv

## Slide 13: DECL Lorries – Generic parametrisation P-HEV strategy
Operation in Charge sustaining (CS) mode
  Dedicated GUI feature available in order to overrule 3 iterations and perform calculation with single individual EF only (for engineering exercise)
  Instructions:
    Copy files from “\Declaration\HEVParameters\Lorry\HEV_Strategy_Parameters_fequiv_XXsoc.csv” to “\Declaration\Override\” without adding any sub-directories
    Adapt respective values for individual EF in files (per vehicle group, mission profile and payload)  1st value for low loading, 2nd for reference loading
vehiclegroup | longhaul | regionaldelivery | urbandelivery | municipalutility | construction
53 |  | 2.6/2.3 | 2.7/2.3 |  | 
54 |  | 2.6/2.3 | 2.7/2.3 |  | 
1s |  | 2.6/2.3 | 2.7/2.3 |  | 
1 |  | 2.6/2.3 | 2.7/2.3 |  | 
2 | 0.1/0.1 | 2.6/2.3 | 2.7/2.3 |  | 
3 |  | 2.6/2.3 | 2.7/2.3 |  | 
4 | 1.4/1.3 | 2.2/2.6 | 1.9/2.3 | 2.1/2.1 | 2.1/2.1
5 | 1.4/1.3 | 2.2/2.6 | 1.9/2.3 |  | 2.1/2.1
… | … | … | … | … | …

## Slide 14: DECL Lorries – Generic parametrisation P-HEV strategy
Operation in Charge sustaining (CS) mode
  Dedicated GUI feature available in order to overrule 3 iterations and perform calculation with single individual EF only (for engineering exercise)
  Instructions:
    Step 3: Activate GUI feature under “Options” tab to apply single run with individually set EF loaded from “\Declaration\Override\” folder
    ATTENTION: Only loaded when VECTO is launched initially (updates during active VECTO session have no effect)!
To be checked: Handling of vehicles with very small batteries in LH (due to high amount of energy being captured at the very end of the cycle)

## Slide 15: Updated P-HEV gear shift model (DECL + ENG)
Gear shift model for P-HEV used slightly wrong ICE operation point for evaluation of fuel costs  mainly relevant for overdrive drivetrain configurations  effect for non-overdrive drivetrains:
  Typical LH application: from slight decrease <1% up to slight increase <1% of HEV FC
  Typical dynamic (urban) application:
    More realistic (higher) acceleration behavior and better following of speed trace like ICE-only counterpart
    Still some percent decrease of FC of HEV compared to previous version
In actual simulation nothing was changed, the change only affects methods used for cost evaluation

## Slide 16: Updated P-HEV gear shift model (DECL + ENG)
Class 4 vehicle on RD reference load;​
Gearbox with direct gear (3% higher η) and overdrive;
Much better results after the update compared to the previous implementation;​
Test​ | Consumption [-]​ | Direct gear usage [% time]​ | Overdrive gear usage [% time]​
ICE ​ | 1​ | 42%​ | 26%​
Direct + overdrive​ | 0.965​ | 7%​ | 68%​
Direct only​ | 0.895​ | 78%​ | -​
Direct + overdrive​ | 0.870​ | 57%​ | 12%​

## Slide 17: Updated time-based with gear mode for AT (ENG only)​
Several manufacturers reported that the TC can be briefly active in higher gears – mainly during gearshifts;​
Allow input of "TC active" signal in vdri in this mode;​
Changes apply only in engineering mode. Included in the upcoming DEV release;​

## Slide 18: DECL Lorries – Generic parametrisation usable SOC range
Actual SOC range used for simulation is determined according to 3 elements:
  Generic SOC range for new vehicle
    Defined separately for PEV, OVC-HEV, Non-OVC-HEV (NOVC-HEV)
  Declared SOC range for new vehicle acc. to Annex III (P413 + P414)
  Deterioration factor applied for half of lifetime
    Preliminary assumption: 5% decrease of usable SOC range (i.e. 0.95 x SOC-range of new vehicle)
  Preliminary figures in table below:
Further discussions regarding final values ongoing  see separate agenda point

## Slide 19: DECL Lorries – Separate approach „CD mode“ simulation
„Frozen“ SOC (infinity battery) at „SOCcenter“ applied (i.e. average of actual SOCmax and SOCmin)  see previous slide
GUI feature to set frozen SOC to other values than „center SOC“ (see figure)
  Value needs to be between actual SOCmax and SOCmin for each individual battery installed
Influence factors on result:
  Limitation of maximum battery power = f(SOC)
  Internal resistance = f(SOC) (i.e. battery losses)
Discussions ongoing which SOC level(s) shall be considered for final method  see separate agenda point

## Slide 20: DECL Lorries – Calculation EC at “battery terminals”
Case PEV:
  Only re-charging in depot relevant for charging losses (since no detailled information in charging behaviour is available)
  Power level for determining charging losses in battery defined by following equation: nominal charging power in kW = max(10, (usable SOC in kWh) / 6h)
    Usable SOC is determined by integration of OCV-data from actual SOCmin to SOCmax
  Charging efficiency is determined as follows:
    Nominal charging current: Charging power above is divided by OCV at SOCcenter (i.e. average of actual SOCmax and SOCmin)
    Charging losses: nominal charging current and internal resistance at SOCcenter
    Charging efficiency: 1 – (charging losses / charging power)

## Slide 21: DECL Lorries – Calculation EC at “battery terminals”
Case OVC-HEV :
  Charging in depot as well as stationary during mission (acc. to generic usage data) relevant for charging losses
  Power level for determining charging losses in battery defined as follows:
    Depot:
      same as for PEV (see previous slide)
      but limited with declared maximum charging power acc. to Annex III (P402)
    Stationary during mission:
      determined from matrix of generic usage data as already defined for OVC-UF calculation (function of vehicle group and mission profile)
      limited with declared maximum charging power acc. to Annex III (P402)
  2 separate values of charging efficiency determined as described on previous slide
     weighted averaging by amount of charged energy for depot and stationary during mission to determine final charging efficiency

## Slide 22: DECL Lorries – Calculation EC at “battery terminals”
Case OVC-HEV calculation example:
  Charging power levels: Depot 10 kW / Stationary during mission 250 kW
  Battery related data and charging currents:
  Charging losses and efficiencies:
  Weighted final charging efficiency:
Energy charged during mission limited by:
Max. charging power
Duration of event
Usable battery capacity
Number of charging events
Real world usage factor (0.5)
Energy charged in depot limited by:
Usable battery capacity
Real world usage factor (0.75)

## Slide 23: DECL Lorries – Calculation EC at “battery terminals”
For further details please refer to: VECTO-DEV WS#9 11.01.2022 (slide 23ff)
Excel will be distributed together with meeting material

## Slide 24: DECL Lorries – Automation of OVC-HEV simulation
OVC-HEV are HEV with external charging feature (“Plug-in HEV”)
  Declared acc. to Annex III (P401)
2 operation modes for OVC-HEV defined in VECTO:
  Charge depleting mode (CD) where the propulsion energy is provided by the electric storage only  results: kWh_el/km, electric range
  Charge sustaining mode (CS) where the propulsion energy is provided by the fuel storage  SOC is balanced over complete cycle, thus no electric energy consumption (kWh_el/km = 0 per definition!)

## Slide 25: DECL Lorries – Automation of OVC-HEV simulation
Separate simulation runs are performed in VECTO for each mode automatically
Separate results for CD and CS are weighted for final result based on utility factor (UF)
  UF is defined as share of electric range in CD mode on total daily mileage of each mission profile
    electric range is defined by:
      Electric energy consumption in the specific mission in [kWh/km] as result from the simulation
      Usable electric energy, which in turn is defined by:
        battery capacity due to initial SOC
        generic assumptions for re-charging during each mission (number and duration of charging events, available charging power from infrastructure)
  Weighted results (fuel or energy consumption) are calculated according to the following equation:

## Slide 26: DECL Lorries – Range calculations
Overview of different ranges in result matrix in VECTO
Electric range | Definition
Actual charge depleting range (RCDA) | The range that can be driven in charge depleting mode based on the usable amount of REESS energy, without any interim charging. (Annex IV)
Equivalent all electric range (EAER) | The part of the actual charge depleting range that can be attributed to the use of electric energy from the REESS, i.e. without any energy provided by the non-electric propulsion energy storage system. (Annex IV) i.e. RCDA mathematically reduced by energy content of fuel used (based on fuel consumption in charge sustaining mode)
Zero CO2 emissions range (ZCER) | The range that can be attributed to energy provided by propulsion energy storage systems considered with zero CO2 impact. (Annex IV)
for OVC-HEV
for PEV

## Slide 27: DECL Lorries – Automation of OVC-HEV simulation
Schematic overview of result matrix in VECTO for CD + CS mode
For further details please refer to: VECTO-DEV WS#13 04.07.2022 (slide 12ff)
Comments:
General structure given by XML schema structure
The "final results" for each mission profile and payload case are always output in the XML element "Total"
FC, CO2, EC in XML element "Total“ are weighted with UF
Ranges in XML element "Total“ are identical to results from CD mode for OVC-HEV
Zero CO2 emissions range equals EAER for OVC-HEV

## Slide 28: DECL Lorries – Automation of OVC-HEV simulation - EX
„Raw“ results by VECTO
Declared / Component data
Calculation of different specific ranges from data above
Relevant for CO2 Standards Regulation, not for weighting of CD+CS results

## Slide 29: DECL Lorries – Automation of OVC-HEV simulation - EX
Generic data
Due to re-charging during mission
Calculation of UF specific ranges from consumption figures (previous slide) and generic data above
RCDA corrected by real world factor
Calculation of UF as share of electric range in CD mode on total daily mileage (163.9 + 32.0 = 195.8 / 480)

## Slide 30: DECL Lorries – Generic e-PTO in MUN cycle
e-PTO applied for PEV and S-HEV in the MUN cycle (generic refuse body)
e-PTO cycle Pel,PTO = f(t) derived from:
  generic hydraulic pump cycle for ICE and the allocated ICE high idle speed
  assuming an average e-PTO efficiency of 80%
Calculation is included time-resolved in the vmod file
Electric energy consumption is considered in electric range for MUN cyle

## Slide 31: DECL Lorries – Known issues with current version
Elements not yet implemented
  Battery connectors / junction box not included  define and implement generic additional resistances (i.e. loss factors)
  Generic P-HEV strategy:  To be tested whether an alternative post-processing method for vehicles with very small batteries is needed as back-up
  Technical elements as resulting from the revision of the CO2 Standards to be added
    Sub-group allocation for the for the newly covered vehicle groups
    Generation of weighted results for vocational vehicles
Elements still under discussion
  Medium lorries mission profile and payload weighting factors (equally weighted, only preliminary)
  Generic SOC min/max ranges and deterioration (only preliminary values)
  Multiple SOC level(s) for VECTO PEV simulation and respective weighting of results

## Slide 32: DECL Lorries – Testing requests and organ. of feedback
Testing requests:
  Test configurations relevant in your portfolio
  Specific analysis regarding open issues as mentioned on slide “Known issues with current version”
Feedback
  Bug reports, questions etc.: please ONLY use JIRA (no specific emails regarding those topics in the upcoming period)
  If there is an urgent need for a meeting before the next DEV workshop (e.g. because of a special problem), this will be announced separately.
  Bug fixing and support
  TUG will focus on finalising the DECL for buses in the coming weeks.
  Topics for the DECL for lorries will be collected and sorted by priority.
  Unless urgent bugfix releases for blocking issues, there will be no new release before May.

## Slide 33: Vecto 0.7.9.2864 JRC Development Version November 2022
Important Note This is a special development release by JRC to validate the time-runs for BEVs.
Changes
  Implementation of measured speed cycle for BEVs (E2, E3, E4, IEPC)
  Implementation of measured speed with gear for BEVs (E2, IEPC)
  Implementation of Pwheel mode for BEVs (E2, E3, E4, IEPC) In this type of cycle, the input field <n> stands for the speed of the electric motor.
  The E2 vehicle job “Generic Vehicles\Engineering Mode\GenericVehicleE2\BEV_ENG_timeruns.vecto” is preconfigured to run time-run cycles.

## Slide 34: Vecto 0.7.9.2741 Development Version June 2022
Changes/Bugfixes
  Implementation of IEPC
  Implementation of IEPC-S
  Implementation of IHPC
  Adaptations HEV-S strategy, SoC correction for HEV-S
  PTO idle drag losses for PEV, adapting PTO idle losses according to 2nd amendment
  Bugfixes
  Hashing tool crashes in .net version 6.0
  Corrected length for BusAux volume calculation

## Slide 35: Modeling of IEPC component
IEPC is modelled as APT-N transmission and electric machine
  Using already available models, same shift strategy as for E2/S2
  Simplified transmission in case of single-speed IEPC
_int signals refer to the out-shaft of the electric motor

## Slide 36: Peculiarities of IEPC
Model parameters (max torque, power maps) refer to IEPC out-shaft
  Internally converted to electric motor
Overload parameters are measured in the gear with the ratio closest to 1
2 options for drag curve acc. to Annex Xb:
  A single drag curve is provided (measured in gear with ratio closest to 1)
  Drag curve for every gear is provided

## Slide 37: Input data for IEPC component
IEPC powertrain architecture definition
  Specific system layout is described by setting of 3 parameters (for detailed description please refer to Annex Xb)
IEPC layout case # | Differential Included | DesignType WheelMotor | DesignTypeWheel MotorMeasured | Layout schematics | Comments
1 | No | No | n.a. |  | Regular axle component required in job file  useage of transmission type „IEPC Transmission – dummy entry“ (allows axle component alone without a min. number of gears)
2 | Yes | No | n.a. |  | No axle component All parameterization via IEPC specific window
3 | No | Yes | 1 |  | Component test performed in L-config acc. to Annex Xb (only one side)  All torque and power values in input data are multiplied with a factor of 2
4 | No | Yes | 2 |  | Component test performed in T-config acc. to Annex Xb (both sides)

## Slide 38: Input data for IEPC component
IEPC General parameters
Parameter name | Description
RotationalInertia | For EM inertia, gearbox parts not to be considered (as for regular transmission components). Reference point for definition of inertia is EM output shaft. Determined in accordance with point 8 of Appendix 8 of Annex Xb.
DifferentialIncluded | Set to ‘true’ in the case a differential is part of the IEPC
DesignTypeWheelMotor | Set to ‘true’ in the case of an IEPC design type wheel motor
DesignTypeWheelMotorMeasured | Input only relevant in the case of an IEPC design type wheel motor, in accordance with paragraph 4.1.1.2 of Annex Xb. Allowed values: ‘1’, ‘2’

## Slide 39: Input data for IEPC component
IEPC performance parameters
Parameter name | Description
Gear data | For each gear: number, ratio, MaxOutputShaftTorque (optional), MaxOutputShaftSpeed (optional)
Overload data | Overload and Continuous operation point and Overload Time For each voltage level separately Measured in gear closest to ratio 1 acc. to Annex Xb
Max/min torque limits | Full load curve (only for one gear closest to ratio 1 acc. to Annex Xb) For each voltage level separately
Drag torque | Only for one voltage level acc. to Annex Xb
Electric power maps | For each gear For each voltage level separately

## Slide 40: IEPC Input Form
Lists with gear entries are synchronized, gears can be added/removed in the gear-list on the right
Definition of IEPC component via “Vehicle \ IEPC-Tab”
Click for specific IEPC GUI-window

## Slide 41: Gearbox Form for IEPC Vehicles
No gearbox file needs to be provided for IEPC with differential included (case 2)
New IEPC gearbox type for all other variants where only the axlegear ratio needs to be provided
Specific Gearbox Type for IEPC. Only requires axlegear to be provided

## Slide 42: Modeling of IHPC component
IHPC transmission is modeled as APT-N
IHPC electric motor is modeled as regular electric motor at position P2
  Gear-dependent power maps
Peculiarities of IHPC
  Drag-curve shall be set to 0 Nm acc. to Annex Xb
For detailed description of component characteristics as well as testing and measurement post-processing methods please refer to Annex Xb

## Slide 43: Input data for IHPC component
IHPC general parameters EM (same as for basic EM component)
Parameter name | Description
RotationalInertia | For EM inertia, gearbox parts not to be considered (as for regular transmission components). Reference point for definition of inertia is EM output shaft. Determined in accordance with point 8 of Appendix 8 of Annex Xb.

## Slide 44: Input data for IHPC component
IHPC performance parameters EM  same as for basic EM component, except multiple El. power maps
Parameter name | Description
Gear data | For each gear: number (needs to match with specifications in gearbox file)
Overload data | Overload and Continuous operation point and Overload Time For each voltage level separately Measured in gear closest to ratio 1 acc. to Annex Xb
Max/min torque limits | Full load curve (only for one gear closest to ratio 1 acc. to Annex Xb) For each voltage level separately
Drag torque | NOT MEASURED acc. to Annex Xb, but input of “0 Nm” drag torque reqired!
Electric power maps | For each gear For each voltage level separately

## Slide 45: Input data for IHPC component
IHPC parameters Gearbox  same as for basic transmission component  transmission type needs to be set to ”IHPC Transmission”
Parameter name | Description
Gear identifier | For each gear (number needs to match with specifications in IHPC file)  Regular axle component to be specified as well
Ratio | For each gear  Regular axle component to be specified as well
Loss Map | For each gear  Methodology how to derive data acc. to Annex Xb (esp. braking side needs to be measured separately as well – as opposed to copy-paste for regular transmission testing)  Regular axle component to be specified as well

## Slide 46: IHPC Input Form
Number of gears need to match
Definition of IHPC component as two separate component parts via #1: “Vehicle \ IHPC-Tab”
#2: “Gearbox”
Click for specific IHPC GUI-window
Item #1: IHPC-EM
Item #2: IHPC-Gearbox
item #1
item #2
Item #2: IHPC-Gearbox
Item #1: IHPC-EM

## Slide 47: Adaptations Serial Hybrid Strategy (1/3)
Observation: GenSet often switching between optimal and maximum power, while operating constantly at optimal power would be sufficient

## Slide 48: Adaptations Serial Hybrid Strategy (2/3)
Minor changes in Serial Hybrid Strategy
  GenSet is switched on as soon as SoC falls below SoC_min
  GenSet is switched off as soon as SoC reaches SoC_target
  GenSet operation points P_opt and P_max:
    In total 4 points defined, for GenSet in regular and in de-rating condition
    SoC_min ≤ SoC < SOC_target: P_opt
    SoC < SoC_min:
      requested el. power > P_opt: GENSET @ P_max
      requested el. power ≤ P_opt: GENSET @ P_opt
  Note: SoC_min shall be above battery’s min SoC

## Slide 49: Adaptations Serial Hybrid Strategy (3/3)
GenSet now always operates in optimal point
Speed profile is unchanged, SoC trace slightly different

## Slide 50: SoC Correction for HEV-S
REESS SoC for HEV is corrected using the engine line
  Engine line makes no sense for HEV-S as the ICE is decoupled from the drivetrain and operates only in certain points
SoC Correction:
… in case the GenSet was on during the simulation
… in case the GenSet was not on during the simulation

## Slide 51: Vecto 0.7.8.2679 Development Version April 2022
Changes/Bugfixes
  Multi-Target Executables in .net 6.0 and .net Framework 4.8 (and .net Framework 4.5, but this will be removed with the next release)
  Implementation Serial Hybrid Vehicles S2, S3, S4
  Implementation APT-S/P with E2 and S2 vehicle architecture
  Correct handling of retarder positions with HEV and PEV, adding axlegear input retarder option
  Update hashing tool to handle new powertrain components (electric motor, battery, supercap)
  Changing EM overload buffer calculation: interpolate between both voltage levels (pre-processing)
  Handling of torque limitations (engine torque limit, boosting torque limits, gearbox torque limits) for P2 architecture
  Connect electric WHR system to REESS in case of hybrid vehicles
  Update LH cycle
  GUI improvements: enable/disable some fields in Job Form, Vehicle Form, and Hybrid Strategy Parameters to simplify user interface and avoid erratic entries.

## Slide 52: Serial Hybrid Implementation
General approach
  Simple operating strategy, not ECMS–based
  Three-point controller for GenSet (off/optimal point/maximum power)
  Operate GenSet in optimal load-points whenever required and possible
  Drivetrain similar to PEV

## Slide 53: Serial Hybrids: GenSet Pre-Processing
Find optimal points for the GenSet
  Iterate from 0 to maximum power of the ICE (20 steps)
  Iterate from ICE idle speed to n95h speed (20 steps)
  Calculate electric power and fuel consumption for all load-points
  Select operating points:
    Maximum electric power, EM de-rated/not de-rated
    Optimal operating point (minimum FC per electric power generated), EM de-rated/not de-rated

## Slide 54: Serial Hybrid Strategy (main principles)
Calculate max. electric power GenSet can provide
Calculate power demand of electric motor, assuming max. electric power (REESS + GenSet)
Depending on drivetrain power demand and SoC turn on ICE and operate GenSet either in optimal point or at maximum power (considering de-rating of GenSet)
Note: SoC_min and SoC_target are parameters of the SerialHybridStrategy, not REESS

## Slide 55: Serial Hybrids: GenSet
When switching on the ICE, it is often not possible to directly operate it in the desired operating point (high ICE speed, too high torque demand due to inertia)  Ramp-up ICE with electric machine switched off (usually 1 or 2 simulation steps) and then turn on the electric machine

## Slide 56: Serial Hybrid Strategy Parameters
MinSoC
TargetSoC

## Slide 58: EM: overload buffer calculated from both voltage levels
Input parameters of EM measured for min and max voltage level
  Overload data
    Continuous Torque
    Overload Torque + Overload Duration
  Maximum and Minimum torque limitations
  Electric power map
Implementation in software:
  From overload data above, thermal buffer is calculated for each voltage level separately (acc. to equations in VECTO user manual )
  Applied values for simulation run are calculated by linear interpolation between two voltage levels, where average of usable SOC range is used
    Overload buffer
    Maximum and Minimum torque limitations
    Continuous Torque

## Slide 59: Consider gearbox MaxTorque limits for HEV
Ref. to ticket nr. 1478+1479
Only relevant for P1 + P2 HEV where EM is located upstream of transmission
Starting Point: ICE FLD
  Crop with max ICE torque declared at vehicle level (per gear) ‘Vehicle/EngineTorqueLimits’ per gear – P196 + P197
  Add boosting torque Boosting limitations for parallel HEV – P415 + P416
  In case of P1 or P2: crop with gearbox max input torque (per gear) MaxTorque – P157
 Torque limits per gear applied by HybridStrategy
Example for P2

## Slide 60: Vecto 0.7.8.xxx Development Version April 2022
Detailed Changes/Bugfixes (See CITnet/Jira)
  [VECTO-1541] - Implement E2/S2 with APT-S/P
  [VECTO-1549] - Error in gearshift behavior for AT transmissions when braking
  [VECTO-1466] - 076.2451 E2 significant increase of calculation time
  [VECTO-1479] - Maximum gearbox torque not respected
  [VECTO-1519] - 077.2457 E2 Gear oscillation
  [VECTO-1520] - 077.2457 P2 Crashing at takeoff
  [VECTO-1531] - ElectricMotor Lookup Maximum Torque: Object reference not set to an instance of an object
  [VECTO-1532] - 077.2547 P2 crashing with 600 RPM idling speed
  [VECTO-1539] - Engine speed ramping up before vehicle halt
  [VECTO-1551] - AT-P Transmission Bus Application: Error during braking phase
  [VECTO-1559] - battery internal resistance curve
  [VECTO-1411] - Switching to new .NET version
  [VECTO-1456] - Cycle Cache in engineering mode
  [VECTO-1478] - Torque limits only apply to ICE
  [VECTO-1521] - Updating tyre dimensions
  [VECTO-1522] - VECTO warning if there are more steered axles than steering pump technologies

## Slide 61: Vecto 0.7.8.xxx Development Version April 2022
Detailed Changes/Bugfixes (See CITnet/Jira)
  [VECTO-1525] - PCC Preprocessing
  [VECTO-1533] - Multi-Target Compilation and .NET Upgrade
  [VECTO-1538] - Transmission ratios limitation of input value to <=25
  [VECTO-1540] - Retarder Types AxleGearInputRetarder
  [VECTO-1543] - Calculation of EM Overload buffer, and continuous torque
  [VECTO-1545] - WHR electric - connect to REESS
  [VECTO-1548] - Update Coach cycle
  [VECTO-1560] - update toolchain for generating usermanual
  [VECTO-1562] - Adapting WHTC Correction Factor weighting for LH Cycle
  [VECTO-1563] - Electric Motor: Calculation of Overload Buffer
  [VECTO-1564] - XML Schema adaptations
  [VECTO-1565] - VECTO warning if there are more steered axles than steering pump technologies
  [VECTO-1569] - Bugfix: Extrapolation warning in PEV shift strategy
  [VECTO-1573] - Update LH Cycle and WHTC correction factor weighting

## Slide 62: Vecto 0.7.7.2547 Development Version December 2021
Changes/Bugfixes
  Implementation APT-N Gearbox + shift strategy
  Update EM model (drag curve independent of voltage level)
  Update EM electric power map interpolation method
  Update user manual
  Update/bugfixes PEV shift strategy (influence of drag curve, error in calculation of costs)
  Bugfix calculation E_EM_off_loss
  Update generic shift lines for PEV E2
  Bugfix post-processing fuel consumption correction bus auxiliaries (in case of no alternator)
  Bugfixes PCC for xEV

## Slide 63: Vecto 0.7.7.2547 Development Version December 2021
General comments (1/x)
  All topics in this section will also be explained in the next xEV workshop #9 on 11.01.2022
  Also topics for testing and feedback will be discussed in this workshop. Until then, no feedback on the distributed version is expected.
  Calculation of overload buffer for EM
    Overload buffer is currently calculated with data for lower voltage level only
    Update of calculation method based on two voltage levels will be implemented once all details reg. the method are clarified
  Propulsion Torque Limits (Vehicle Boosting Limits)
    In the rotational speed range from 0 to engine idling speed the full load torque available from the ICE equals the ICE full load torque at engine idling speed due to the modelling of the clutch behaviour during vehicle starts.
    Any arbitrary number of values may be declared in between the range of zero and the maximum rotational speed of the ICE full load curve.
    Declared values lower than zero are not allowed for the additional torque.
    For detailed explanation refer to user manual (“Vehicle Editor – Torque Limits Tab”, “Torque and Speed Limitations”)
  Pulse-duration dependency of internal resistance of battery
    For detailed explanation refer to user manual
  HEV operation strategy method for declaration mode
    Method explained in “User Manual/HEV_DECL_method_20211221.pptx” distributed together with VECTO archive
    Generic values defined per (vehicle group, mission, payload and usable SOC range) in “User Manual/HEV_Strategy_Parameters.xlsx” distributed together with VECTO archive
    For further details refer to distributed material/recording from xEV workshop #8

## Slide 64: Vecto 0.7.7.2547 Development Version December 2021
General comments (2/x)
  Auxiliaries for PEV
    Electric power demand of auxiliaries for both, lorries and buses, need to be parameterized via the “BusAux” GUI window
  Gearshift model for PEV
    Details explained on next slides
Demand during vehicle driving
Demand during vehicle standstill

## Slide 65: Vecto 0.7.7.2547 Development Version December 2021
Gearshift model for PEV (1/x)
Basics:
  Downshift for operation point left of green dot-dashed downshift lines
  Upshift for operation point right of green dot-dashed upshift line
  EffShift method applied for operation point between downshift and upshift lines (refer to user manual)
Driving:
  Maximum downshift speed always located at n_P80low (where 80% of max power is available)
  For EM in de-rating n_P80low is calculated from the de-rated power curve
Braking:
  EffShift is suppressed for operation point within red shaded area (2% below max recuperation power)
  New gear after downshift is selected so that operation point is closest to and above n_brake_target_norm (or only closest to n_brake_target_norm in case no operation point with higher speed exists)

## Slide 66: Vecto 0.7.7.2547 Development Version December 2021
Gearshift model for PEV (2/x)
All factors in bold red can be tuned via shift parameter file .vtcu
  Refer to sample file for User Manual/PEV_ShiftParameters.vtcu distributed together with VECTO archive

## Slide 67: Vecto 0.7.7.2547 Development Version December 2021
Detailed Changes/Bugfixes (see CITnet/JIRA)
  [VECTO-1460] - APT-N Gearbox
  [VECTO-1501] - Update EM Map interpolation method
  [VECTO-1477] - Update user manual
  [VECTO-1383] - E2 PEV, 2-speed AMT: "Failed to find operating point"
  [VECTO-1384] - E2 PEV, 2-speed AMT: Downshifts missing
  [VECTO-1414] - E2 selects high gear at low speed after take-off, does not reach target acc
  [VECTO-1443] - 0.7.5.2356 EC_el_final calculated from REESS terminal signals
  [VECTO-1445] - 073.2356, E2 Missing Downshifts, simulation abort
  [VECTO-1464] - Engine Off not working with activated PCC (Hybrid Vehicles)
  [VECTO-1465] - PEV PCCState oscillates between Interrupt and UseCase1
  [VECTO-1467] - PCC HEV Small Spike at end of UseCase1 when Target speed is reached
  [VECTO-1468] - EM map interpolation comments
  [VECTO-1470] - 076.2463 EM drag torque questions/findings
  [VECTO-1482] - Hybrid Vehicle EM speed gets very high, no gearshift
  [VECTO-1483] - Job aborting: E4_Group 5 LH_ll_LongHaul_mod5_id_2
  [VECTO-1484] - Job aborting: P2_Group5_s2c0_rep_Payload_LongHaul_mod5_id_27
  [VECTO-1486] - NG PI fuel type not working with Engine GUI (.veng) in Engineering Mode
  [VECTO-1487] - Calculation of EM efficiency during recuperation
  [VECTO-1490] - Exceeded max iterations: Operating Point could not be found

## Slide 68: Vecto 0.7.7.2547 Development Version December 2021
Detailed Changes/Bugfixes (see CITnet/JIRA)
  [VECTO-1491] - Electric Energy Storage Editor does not show values
  [VECTO-1499] - Energy balance when ICE is turned on in a P1 hybrid configuration
  [VECTO-1514] - Modeldata uses wrong inertia in case multiple EMs are used on a position
  [VECTO-1515] - Output in vsum file
  [VECTO-1516] - GUI: PEV vehicle, disable hybrid parameters
  [VECTO-1489] - Engine-off eco-roll for P1 hybrids
  [VECTO-1448] - 075.2356, E2 Selecting high gear in downhill, needs to use wheel brakes
  [VECTO-1472] - Do not end PCC if acceleration is still high enough
  [VECTO-1473] - Additional tyre dimensions
  [VECTO-1476] - Update EM GUI, EM component
  [VECTO-1493] - Use EngineStartStop in PCC-Events for Hybrid P1
  [VECTO-1498] - Crosswind correction in engineering mode
  [VECTO-1508] - EM-Off Losses in .vsum
  [VECTO-1509] - SP Technology "Electric" already contains mechanical power demand
  [VECTO-1510] - Remove selection of shift strategy in job dialog
  [VECTO-1511] - Error Message for "HEVs and BEVs not supported in Declaration Mode"
  [VECTO-1512] - Adapt shift lines for xEV vehicles
  [VECTO-1513] - Bus Aux post-processing correction
  [VECTO-1481] - New warning message regarding transmission: what does it mean?

## Slide 69: Vecto 0.7.6.2451 Development Version September 2021
Changes
  ADAS for HEV and PEV vehicles
    For HEV vehicles interaction of PCC and HEV strategy under further analysis
  Update electric motor model: support for different voltage levels
  Update battery model: modular battery components
  Update battery model: pulse-duration dependent internal resistance
  Bugfixes

## Slide 70: Vecto 0.7.5.2353 Development Version June 2021
Changes
  Bugfixes in shift strategy for PEV (E2)
  Additional Powertrain architectures
    P1 AMT and APT-S/P
    P2.5 (transmission ratio EM per gear)
    P3 & P4 with APT transmissions
  Loss-map for electric machine
  Bus auxiliaries in engineering mode
  Combine Bus auxiliaries with HEV powertrains
  Refactoring Engine Stop/Start approach
    ICE is always off during simulation, balance missing energy in case ICE is on / ICE is off for all auxiliaries in .vmod.
    Correct for missing aux energy in post-processing (not fully implemented in this version)
  Added vehicle propulsion limits (relative to ICE max torque)
    P2, P3, and P4
  Refactored EM model: continuous torque, overload torque as separate inputs

## Slide 71: Vecto 0.7.3.2164 Development Version December 2020
Changes
  Bugfixes in shift strategy for PEV (E2)
  Refined electric motor model: model transmission stage of electric machine as individual sub-component instead of transforming the maps. Adapted columns in .vmod and .vsum regarding electric machine. See user manual for details.
  Bugfixes SuperCap model
  Removed E_REESS from .vmod file, calculate delta_E_REESS from P_REESS in .vsum file

## Slide 72: Vecto 0.7.2.2118 Development Version October 2020
Changes
  Implementation of PEV architecture E2 with EffShift-like gearshift strategy
  Bugfix REESS Dialog (.vimax)
  Bugfix in output of EM overload output in .vmod file

## Slide 73: Vecto 0.7.1.2108 Development Version October 2020
Changes
  More stable operating point search hybrid strategy
  Bugfixes hybrid strategy
  Adding Super Cap as REESS
  Adding electric machine thermal de-rating
  Modified battery model: max charge/discharge current over state of charge
  Improvements simulation time hybrid vehicles
Note: As the model data for electric machine and battery changed from the previous VECTO version for hybrid vehicles it is necessary to open the models and provide the newly added model parameters.

## Slide 74: Vecto 0.7.0.2076 Development Version September 2020
Changes
  This release is the first beta version with capabilities to simulate hybrid and battery electric vehicles.
  It covers powertrain architectures “P2”, “P3”, “P4” for hybrid electric vehicles (HEV) and “E3”, “E4” for battery electric vehicles (PEV, pure electric vehicles).
  The definitions of the powertrain architectures and other input parameters on vehicle level can be found in the document Input parameters vehicle level 20200907.docx. This document is an excerpt of working document 3 of the HDV CO2 Editing board. Items marked in red are not yet featured by the tool and will follow in the next releases.
  Known limitations
    Electric machine system overload feature not available – work in progress
    Supercaps not implemented – work in progress
    Engine Stop Start Utility Factor has to be set to 1 – further discussions in task force needed how UF-approach shall be aligned with hybrid control strategy
    P_aux_el are electric auxiliaries connected to the high-voltage system. For hybrid electric vehicles this model parameter shall currently be set to 0. – further discussions in task force needed
    APTs with HEV – to be implemented
    Eco-roll and PCC not implemented

## Slide 75: Vecto 0.6.1.1975 Development Version May 2020
Bugfixes
  Change passenger density primary vehicle for IU cycle
  primary vehicle: ignore TPMLM (to limit payload, do not abort simulation)
  completed vehicle: limit total mass with TPMLM (abort simulation)
  consider l_drivetrain. this length is subtracted from internal length for HVAC calculation only (bus volume for ventilation, max cooling capacity); completed vehicle
  set alternator gear efficiency to 1 to align with lorries (currently 0.92)
  electric system / radio: all vehicles are equipped with radio. modify consumed amps to consider 'usage factor' - updated already in master excel.
  Update generic values for primary HF vehicles CdxA
  HVAC: check/correct internal height for coaches (shall be 1.8m)
  HVAC: subtract driver compartment from total volume for max cooling capacity passengers
  HVAC: add configuration #10, add sanity checks (i.e. if driver AC is provided for configurations #2,
  Steering pump power demand: tubing factor only applied for first steered axle (as the additionally steered axles are close to the engine and the distance is not known)
  Allow enabling/disabling LAC in declaration mode via GUI (not persistent). Additional input on “Options” tab to set min activation speed
  .vsum file: E_AUX_SUM matches sum of individual AUX entries; bugfix writing P_busAux_ES_mech
  Update user manual on VTP cycle file format
  APT gearbox (all gears) generic efficiency 0.925
  retarder: set factor for generic retarder losses from 0.5 to 1 (i.e., use standardvalues)
  VTP engineering mode - vsum actual CF different to declaration mode
Improvements
  Switch GUI to 64bit mode (see VECTO-1270)
  New normalization/denormalization method for generic engine FC-Map (see VECTO-1269)
  .vsum-file: new entries P_ice_fcmap, P_wheel_in, k_vehline (previous k_vehline is now k_engline
  Bus VTP: Fan Parameter C4
  don't write CIF for primary vehicle

## Slide 76: Vecto 0.6.1.1957 Development Version May 2020
Improvements
  Declaration mode for complete and completed buses via “factor method”
  VTP mode for heavy buses
  VTP mode for dual-fuel vehicles (new cycle file required!)
  “Single bus” mode with generic data from segmentation table completed vehicle (previous version used generic data from primary vehicle)
  Adding highway sections on coach cycle (required for PCC)
  New graphical user interface (VECTO3.exe) (alpha version!)
    Creating & editing complete(d) bus XML
    Creating & editing complete(d) bus job file (PIF + completed XML)
    Creating & editing single bus job file (primary XML + completed XML)
    Simulation of all types of VECTO jobs
    Currently, other existing job files can not be edited in the new GUI – planned to be extended in future
    Functionality similar to currently official VECTO version, for further information see separate user manual on new GUI
  XML reports (MRF, CIF, PIF) according to draft Annex IV
  Expert feature: allow adding torque converter data to PIF manually (not added by VECTO automatically) to investigate on generic TC data for APT-P (see generic vehicles for reference)
  Expert feature: allow writing internal model data used for VECTO simulation as JSON file. Allows to compare model data between primary bus, completed bus generic body, completed bus specific body (factor method) as well as single bus

## Slide 77: Vecto 0.6.1.1957 Development Version May 2020
Bugfixes heavy buses
  Correcting power demand for engine fan
  Consider electric auxiliaries (fan, steering pump) as electrical consumer
  Correcting power demand pneumatic system with mechanical clutch
  Correcting electrical consumers LED bonus
  Correction for double compensation of smart electrics (battery & generated vs. consumed)
  Correcting passenger count depending on HVAC configuration
Bugfixes medium lorries
  New technologies for electric steering pump
  New tyre xml supported
  Bugfixes graphical user interface
  New sample data VTP

## Slide 78: Vecto 0.6.0.1908 Development Version March. 2020
Bugfixes
  Consider vehicle’s max speed when validating input data, calculating velocity drop during traction interruption
  Reading vehicle design speed (85km/h) from segment table (also related to vehicle’s max speed)
  Fix JobEditor GUI – toolbar with icons not visible
  Fix null-reference exception simulating vehicles in engineering mode

## Slide 79: Vecto 0.6.0.1884 Development Version Feb. 2020
Improvements
  Refactoring and bug fixes in bus auxiliaries model (former Ricardo AAUX model), parametrization of bus auxiliaries model (HVAC) from “primary bus” input data and generic values in segmentation matrix,
  Support for P0 hybrids in bus auxiliaries model
  Support for “primary bus” (declaration mode)
  Support for “single bus” – combine input parameters of primary bus and completed bus to a single simulation (no factor method) (declaration mode)
  Support for medium lorries
  Support for vehicles with front-wheel drive (axlegear included in gearbox)
  VTP Mode for medium lorries
  New XML schema for new vehicle categories, adapted XML schema for generated reports (MRF, CIF, PIF)
This development version includes all features already included in version 0.5.0

## Slide 80: Vecto 0.5.0 Development Version Dec. 2019
Improvements
  Adding in-the-loop simulation of advanced driver assistant systems (ADAS)
    Engine stop-start during vehicle stop
    Eco-roll with and without engine stop
    Predictive cruise control: dip coasting, crest coasting
  Adding support for dual-fuel vehicles
  Adding support for waste- / exhaust-heat recovery systems (electrical and mechanical)
  New gear shift strategy (EffShift) for AMT and AT transmissions
Details on the new models, model parameters, and new signals in the output are described in the user manual

## Slide 81: Vecto 3.3.10.2401 Official Release 2020-07-29
Improvements
  Handling of exempted vehicles (not changed since release candidate) – see next slides for details
Bugfixes
  No additional bugfixes compared to VECTO 3.3.10.2401

## Slide 82: Vecto 3.3.10.2373 Release Candidate 2020-07-01
Improvements
  [VECTO-1421] – Added vehicle sub-group (CO2-standards to MRF and CIF)
  [VECTO 1449] – Handling of exempted vehicles: See next slide for details
  [VECTO-1404] – Corrected URL for CSS in MRF and CIF
Bugfixes
  [VECTO-1419] – Simulation abort in urban cycle: failed to find operating point on search braking power with TC gear
  [VECTO-1439] – Bugfix handling duplicate entries in engine full-load curve when intersecting with max-torque of gearbox
  [VECTO-1429] – error in XML schema 2.x for exempted vehicles – MaxNetPower1/2 are optional input parameters

## Slide 83: Vecto 3.3.10.2373 Release Candidate 2020-07-01
Handling of exempted vehicles
Axle configuration and sleeper cab are optional input parameters for exempted vehicles (XML schema 1.0 and 2.2.1).
  OEMs are recommended to provide these parameters for exempted vehicles.
  If the axle configuration is provided as input parameter, the MRF contains the vehicle group.
  The sleeper cab input parameter is also part of the MRF if provided as input.
Input parameters MaxNetPower1/2 are optional input parameters for all exempted vehicles.
  If provided in the input these parameters are part of the MRF for all exempted vehicle types
  It is recommended that those parameters are used to specify the rated power also for PEV (pure electric vehicles)

## Slide 84: Vecto 3.3.9.2175 Official Release 2020-12-15
Bugfixes (compared to version 3.3.9.2147)
  [VECTO-1374] - VECTO VTP error – regression update

## Slide 85: Vecto 3.3.9.2147 Release Candidate 2020-11-17
Bugfixes
  [VECTO-1331] - VTP Mode does not function for vehicles of group 3
  [VECTO-1355] - VTP Simulation Abort
  [VECTO-1356] - PTO Losses not considered in VTP simulation
  [VECTO-1361] - Torque Converter in use for the First and Second Gear VTP file does not allow for this
  [VECTO-1372] - Deviation of CdxA Input vs. Output for HDV16
  [VECTO-1374] - VECTO VTP error
Improvements
  [VECTO-1360] - make unit tests execute in parallel

## Slide 86: Vecto 3.3.8.2052 Official Release 2020-08-14
Bugfixes
  No additional bugfixes compared to VECTO 3.3.8.2024

## Slide 87: Vecto 3.3.8.2024 Release Candidate 2020-07-17
Bugfixes
  [VECTO-1288] - Simulation Abort UD RL
  [VECTO-1327] - Simulation abort Construction RefLoad: unexpected response ResponseOverload
  [VECTO-1266] - Gear 4 Loss-Map was extrapolated

## Slide 88: Vecto 3.3.7.1964 Official Release 2020-05-18
Bugfixes
  [VECTO-1254] - Hashing method does not ignore certain XML attributes
  [VECTO-1259] - Mission profile weighting factors for vehicles of group 16 are not correct

## Slide 89: Vecto 3.3.6.1916 Official Release 2020-03-31
Bugfixes
  [VECTO-1250] - Error creating new gearbox file from scratch

## Slide 90: Vecto 3.3.6.1898 Release Candidate 2020-03-13
Improvement
  [VECTO-1239] - Adaptation of Mission Profile Weighting Factors
  [VECTO-1241] - Engineering mode: Adding support for additional PTO activations
Bugfixes
  [VECTO-1243] - Bug in VTP mode for heavy lorries
  [VECTO-1234] - urban cycle at reference load not running for bug when find braking operating point

## Slide 91: Vecto 3.3.5.1812 Official Release 2019-12-18
Bugfixes (compared to VECTO 3.3.5.1783-RC)
  [VECTO-1220] - Simulation Abort Urban Delivery RefLoad

## Slide 92: Vecto 3.3.5.1783 Release Candidate 2019-11-19
Improvement
  [VECTO-1194] - Handling input parameter 'vocational' for groups other than 4, 5, 9, 10
  [VECTO-1147] - Updating declaration mode cycles values in user manual
  [VECTO-1207] - run VECTO in 64bit mode by default
Bugfixes
  [VECTO-1074] - Vecto Calculation Aborts with Interpolation Error
  [VECTO-1159] - Simulation Abort in UrbanDelivery LowLoading
  [VECTO-1189] - Error in delaunay triangulation invariant violated
  [VECTO-1209] - Unexpected Response Response Overload
  [VECTO-1211] - Simulation Abort Urban Delivery Ref Load
  [VECTO-1214] - Validation of input data fails when gearbox speed limits are applied

## Slide 93: Vecto 3.3.4.1716 Official Release 2019-09-13
Bugfixes (compared to VECTO 3.3.4.1686-RC)
  [VECTO-1074] - Vecto Calculation Aborts with Interpolation Error ([VECTO-1046])
  [VECTO-1111] - Simulation Abort in Municipal Reference Load

## Slide 94: Vecto 3.3.4.1686 Release Candidate 2019-08-14
Improvement
  [VECTO-1042] - Add option to write results into a certain directory
  [VECTO-1064] - add weighting factors for vehicle groups 1, 2, 3, 11, 12, 16
Bugfixes
  [VECTO-1030] - Exceeded max iterations when searching for operating point! Failed to find operating point!
  [VECTO-1032] - Gear 5 LossMap data was extrapolated in Declaration Mode: range for loss map is not sufficient
  [VECTO-1067] - Vair and Beta correction for Aerodynamics
  [VECTO-1000] - Error Loss-Map extrapolation in Declaration Mode
  [VECTO-1040] - Gear 6 LossMap data was extrapolated in Declaration Mode
  [VECTO-1047] - Failed to find operating point on construction cycle, ref load, AT gearbox

## Slide 95: Vecto 3.3.3.1639 Official Release 2019-06-27
Bugfixes (compared to VECTO 3.3.3.1609-RC)
  [VECTO-1003] - Vecto Error: Loss-Map extrapolation in declaration mode required (issue VECTO-991)
  [VECTO-1006] - Failed to find torque converter operating point on UD cycle (issue VECTO-996)
  [VECTO-1010] - Unexpected Response: ResponseOverload in UD cycle (issue VECTO-996)
  [VECTO-1015] - XML Schema not correctly identified
  [VECTO-1019] - Error opening job in case a file is missing
  [VECTO-1020] - HashingTool Crashes
  [VECTO-1021] - Invalid hash of job data

## Slide 96: Vecto 3.3.3.1609 Release Candidate 2019-05-29
Improvement
  [VECTO-916] - Adding new tyre sizes
  [VECTO-946] - Refactoring XML reading
  [VECTO-965] - Add input fields for ADAS into VECTO GUI
  [VECTO-966] - Allow selecting Tank System for NG engines in GUI
  [VECTO-932] - Consistency in NA values in the vsum file
Bugfixes
  [VECTO-954] - Failed to find operating point for braking power (Fix for Notification Art. 10(2) - [VECTO-952])
  [VECTO-979] - VECTO Simulation abort with 8-speed MT transmission (Fix for Notification Art. 10(2) - [VECTO-978])
  [VECTO-931] - AT error in VECTO version 3.3.2.1519
  [VECTO-950] - Error when loading Engine Full-load curve
  [VECTO-967] - Engine-Only mode: Engine Torque reported in .vmod does not match the provided cycle
  [VECTO-980] - Error during simulation run

## Slide 97: Vecto 3.3.2.1548 Official Release 2019-03-29
Bugfixes (compared to 3.3.2.1519-RC)
  [VECTO-861] - 3.3.1: Torque converter not working correctly
  [VECTO-904] - Range for gear loss map not sufficient.
  [VECTO-909] - 3.3.2.1519: Problems running more than one input .xml
  [VECTO-917] - TargetVelocity (0.0000) and VehicleVelocity (>0) must be zero when vehicle is halting
  [VECTO-918] - RegionalDeliveryEMS LowLoading - ResponseSpeedLimitExceeded
  [VECTO-920] - Urban Delivery: Simulation Run Aborted, TargetVelocity and VehicleVelocity must be zero when vehicle is halting!

## Slide 98: Vecto 3.3.2.1519 Release Candidate 2019-03-01
Improvements
  [VECTO-869] - change new vehicle input fields (ADAS, sleeper cab, etc.) to be mandatory
  [VECTO-784] - Configuration file for VECTO log files
  [VECTO-865] - Extend Sum-Data
  [VECTO-873] - Add digest value to SumData
Bugfixes
  [VECTO-729] - Bugs APT submodel
  [VECTO-787] - APT: DrivingAction Accelerate after Overload
  [VECTO-789] - APT: ResponseUnderload
  [VECTO-797] - VECTO abort with AT transmission and TC table value
  [VECTO-798] - VECTO abort with certified AT transmission data and certified TC data
  [VECTO-807] - VECTO errors in vehicle class 1/2/3
  [VECTO-827] - Torque converter inertia
  [VECTO-838] - APT: ResponseOverload
cont.

## Slide 99: Vecto 3.3.2.1519 Release Candidate 2019-03-01
Bugfixes
  [VECTO-843] - AT Transmissions problem on VECTO 3.3.1.1463
  [VECTO-844] - Error with AT gearbox model
  [VECTO-847] - Simulation abort due to error in NLog?
  [VECTO-848] - AT Gearbox Simulation abort (was: Problem related to Tyres?)
  [VECTO-858] - Urban Delivery Abort - with APT-S Transmission and TC
  [VECTO-861] - 3.3.1: Torque converter not working correctly
  [VECTO-872] - MRF/CIF: Torque Converter certification method and certification nbr not correctly set
  [VECTO-879] - SIMULATION RUN ABORTED DistanceRun got an unexpected resp.
  [VECTO-883] - Traction interruption may be too long
  [VECTO-815] - Unexpected Response: SpeedLimitExceeded
  [VECTO-816] - object reference not set to an instance of an object
  [VECTO-817] - TargetVelocity and VehicleVelocity must not be 0
  [VECTO-820] - DistanceRun got an unexpected response: ResponseSpeedLimitExceeded
  [VECTO-864] - Prevent VECTO loss-map extension to result in negative torque loss

## Slide 100: Vecto 3.3.2.1519 Release Candidate 2019-03-01
Installation Option (VECTO-784)
  VECTO 3.3.2 adds a new feature to run as ‘installed application’ instead of the ‘portable’ mode
  VECTO as ‘installed application’
    Needs no write permissions to the VECTO application folder
    All configuration files and settings are written to %AppData%\VECTO\<Version>
    All log files are written to %LocalAppData%\VECTO\<Version>
  Switch to ‘installed application’
    Copy the VECTO directory and all its files and subdirectories to the appropriate location where the user has execute permissions
    Edit the file ‘install.ini’ and remove the comment character (#) in the line containing ExecutionMode = install

## Slide 101: Vecto 3.3.1.1492 Official Release 2019-02-01
Bugfixes (compared to 3.3.1.1463-RC)
  [VECTO-845] - Fixing bug for VECTO-840
  [VECTO-826] - DistanceRun got an unexpected response: ResponseSpeedLimitExceeded
  [VECTO-837] - VECTO GUI displays incorrect cycles prior to simulation
  [VECTO-831] - Addition of indication to be added in Help and Release notes for simulations with LNG
cont.

## Slide 102: Vecto 3.3.1.1463 Release Candidate 2019-01-03
Changes according to 2017/2400 amendments
  [VECTO-761] - Adaptation of input XML Schema
  [VECTO-762] - Extension of Input Interfaces
  [VECTO-763] - Extension of Segmentation Table
  [VECTO-764] - ADAS benefits (according to Annex III Point 8. of amendment to 2017/2400)
  [VECTO-766] - Update power demand auxiliaries (for extended segmentation table)
  [VECTO-767] - Report for exempted vehicles
  [VECTO-768] - VTP mode
  [VECTO-770] - Fuel Types
  [VECTO-771] - Handling of exempted vehicles
  [VECTO-824] - Throw exception for certain combinations of exempted vehicle parameters
  [VECTO-773] - Correction Factor for Reference Fuel
  [VECTO-790] - Adapt generic data for construction/municipal utility
  [VECTO-493] - Implementation of generic body weights and air drag values for construction cycle
  [VECTO-565] - Consideration of LNG as possible fuel is missing
cont.

## Slide 103: Vecto 3.3.1.1463 Release Candidate 2019-01-03
New input parameters
  The new input fields (see table below) are optional in this version. When this release candidate will be an official version manufacturers MAY certify their new vehicles using the new input parameters. As from 1st July 2019 the new input fields will become mandatory. Further details are provided in the timetable on the next page.
  Default values when the new input parameters are not provided:
cont.
Input parameters vehicle – Table 1 Annex III | 
Field | Default value
VehicleCategory | No default value but input 'rigid truck' will be converted automatically into 'rigid lorry'
ZeroEmissionVehicle | 'No'
NgTankSystem | 'Compressed' (only applicable to gas vehicles)
SleeperCab | 'Yes'
Input parameters ADAS – Pt. 8 Annex III | 
Field | Default value
EngineStartStop | 'No'
EcoRollWithoutEngineStop | 'No'
EcoRollWithEngineStop | 'No'
PredictiveCruiseControl | 'No'
  Currently only the fuel type ‘NG PI’ for the engine certification is allowed by 2017/2400. For LNG vehicles, therefore, the engine fuel type has to be set to ‘NG PI’ and at the vehicle level NgTankSystem has to be set to liquefied. For CNG the same engine fuel type is used but NgTankSystem has to be set to compressed.

## Slide 104: Vecto 3.3.1.1463 Release Candidate 2019-01-03
Timetable
cont.
Planned Date | Version | Description
1. Feb. 2019 | 3.3.1.x | Release of official version of release candidate 3.3.1.1463
1. March 2019 | 3.3.2.x-RC | Release candidate, new input parameters are mandatory (+ further bugfixes)
1. April 2019 | 3.3.2.x | Official version of VECTO 3.3.2
1. May 2019 |  | Mandatory use of 3.3.1.x for certification
1. July 2019 |  | Mandatory use of 3.3.2.x for certification

## Slide 105: Vecto 3.3.1.1463 Release Candidate 2019-01-03
Changes/Improvements
  [VECTO-799] - Remove TUG Logos from Simulation Tool, Hashing Tool
  [VECTO-808] - Add Monitoring Report
  [VECTO-754] - Extending Loss-Maps in case of AT gearbox for each gear, axlegear, gearbox
  [VECTO-757] - Correct contact mail address in Hashing Tool
  [VECTO-779] - Update Construction Cycle - shorter stop times
  [VECTO-783] - Rename columns in segmentation table and GUI
  [VECTO-709] - VTP editor from user manual not matching new VECTO one: updated documentation
  [VECTO-785] - Handling of Vehicles that cannot reach the cycle's target speed: Limit max speed in driver model
  [VECTO-716] - Validate data in Settings Tab: update documentation
  [VECTO-793] - Inconsistency between GUI, Help and Regulation: update wording in GUI and user manual
  [VECTO-796] - Adaptation of FuelProperties
  [VECTO-806] - extend loss-maps (gbx, axl, angl) for MT and AMT transmissions
  [VECTO-750] - Simulation error DrivingAction: adapt downshift rules for AT to drive over hill with 6% inclination
cont.

## Slide 106: Vecto 3.3.1.1463 Release Candidate 2019-01-03
Update of Fuel Properties [VECTO-796]
cont.
Fuel type | Reference for fuel properties | Density | CO2 emission factor | Lower Heating Value | Data Source
[-] | [-] | [kg/m³] | [g_CO2/g_Fuel] | [MJ/kg] | [-]
Diesel | B7 | 836 | 3.13 | 42.7 | CONCAWE/JEC (2018)
ED95 | ED95 | 820 | 1.81 | 25.4 | CONCAWE/JEC (2018)
Petrol | E10 | 748 | 3.04 | 41.5 | CONCAWE/JEC (2018)
E85 | E85 | 786 | 2.10 | 29.3 | Calculated from E0 and E100 from CONCAWE/JEC (2018)
LPG | LPG | not required* | 3.02 | 46.0 | CONCAWE/JEC (2018)
CNG | CNG (H-Gas) | not required* | 2.69 | 48.0 | CONCAWE/JEC (2018)
LNG | LNG (EU mix. 2016/2030) | not required* | 2.77 | 49.1 | CONCAWE/JEC (2018)
* VECTO does not provide volume based figures for gaseous fuels |  |  |  |  | 
CONCAWE/JEC (2018): Specifications are based on a recent analysis (2018) performed by CONCAWE/EUCAR and shall reflect typical fuel on the European market. The data is scheduled to be published in March 2019 in the context of the study: Well-To-Wheels Analysis Of Future Automotive Fuels And Powertrains in the European Context – Heavy Duty vehicles

## Slide 107: Vecto 3.3.1.1463 Release Candidate 2019-01-03
Bugfixes
  [VECTO-819] - object reference not set to an instance of an object
  [VECTO-818] - SearchOperatingPoint: Unknown response type. ResponseOverload
  [VECTO-813] - Error "Infinity [] is not allowed for SI-Value"
  [VECTO-769] - DrivingAction Brake: request failed after braking power was found.ResponseEngineSpeedTooHigh
  [VECTO-804] - Error on simulation with VECTO 3.3.0.1433
  [VECTO-805] - Total vehicle mass exceeds TPMLM
  [VECTO-811] - AMT: ResponseGearShift
  [VECTO-812] - AMT: ResponseOverload
  [VECTO-822] - SIMULATION RUN ABORTED by Infinity
  [VECTO-792] - Vecto Hashing Tool - error object reference not set to an instance of an object (overwriting Date element)
  [VECTO-696] - Problem with Primary Retarder: regression update, set torque loss to 0 for 0 speed and engaged gear
  [VECTO-776] - Decision Factor (DF) field is emptied after each simulation
  [VECTO-814] - Error: DistanceRun got an unexpected response: ResponseGearshift

## Slide 108: Vecto 3.3.0.1433 Official Release 2018-12-04
Bugfixes (compared to 3.3.0.1398)
  [VECTO-795] – VECTO Hashing Tool crashes
  [VECTO-802] – Error in XML schema for manufacturer's record file
Bugfixes (compared to 3.3.0.1250)
  [VECTO-723] - Simulation aborts with engine speed too high in RD cycle
  [VECTO-724] - Simulation aborts with error 'EngineSpeedTooHigh' - duplicate of VECTO-744
  [VECTO-728] - Simulation aborts when vehicle's max speed (n95h) is below the target speed
  [VECTO-730] - Simulation Aborts with ResponseOverload
  [VECTO-744] - ResponseEngineSpeedTooHigh (due to torque limits in gearbox)
  [VECTO-731] - Case Mismatch - Torque Converter
  [VECTO-711] - Elements without types in CIF and MRF
  [VECTO-757] - Correct contact mail address in Hashing Tool
  [VECTO-703] - PTO output in MRF file
  [VECTO-713] - Manufacturer Information File in the legislation is not compatible with the Simulation results
Improvement (compared to 3.3.0.1250)
  [VECTO-704] - Allow VTP-simulations for AT gearboxes

## Slide 109: Vecto 3.3.0.1398 Release Candiate 2018-10-30
Bugfixes
  [VECTO-723] - Simulation aborts with engine speed too high in RD cycle
  [VECTO-724] - Simulation aborts with error 'EngineSpeedTooHigh' - duplicate of VECTO-744
  [VECTO-728] - Simulation aborts when vehicle's max speed (n95h) is below the target speed
  [VECTO-730] - Simulation Aborts with ResponseOverload
  [VECTO-744] - ResponseEngineSpeedTooHigh (due to torque limits in gearbox)
  [VECTO-731] - Case Mismatch - Torque Converter
  [VECTO-711] - Elements without types in CIF and MRF
  [VECTO-757] - Correct contact mail address in Hashing Tool
  [VECTO-703] - PTO output in MRF file
  [VECTO-713] - Manufacturer Information File in the legislation is not compatible with the Simulation results
Improvement
  [VECTO-704] - Allow VTP-simulations for AT gearboxes

## Slide 110: Vecto 3.3.0.1250 2018-06-04
Improvement
  [VECTO-665] - Adding style information to XML Reports
  [VECTO-669] - Group 1 vehicle comprises vehicles with gross vehicle weight > 7.5t
  [VECTO-672] - Keep manual choice for "Validate data"
  [VECTO-682] - VTP Simulation in declaration mode
  [VECTO-652] - VTP: Check Cycle matches simulation mode
  [VECTO-683] - VTP: Quality and plausibility checks for recorded data from VTP
  [VECTO-685] - VTP Programming of standard VECTO VTP report
  [VECTO-689] - Additional Tyre sizes
  [VECTO-702] - Hashing tool: adapt warnings
  [VECTO-667] - Removing NCV Correction Factor
  [VECTO-679] - Engine n95h computation gives wrong (too high) engine speed (above measured FLD, n70h)
  [VECTO-693] - extend vehicle performance in manufacturer record

## Slide 111: Vecto 3.3.0.1250 2018-06-04
Bugfixes
  [VECTO-656] - Distance computation in vsum
  [VECTO-666] - CF_RegPer no effect in vehicle simulation -- added to the engine correction factors
  [VECTO-687] - Saving a Engine-Only Job is not possible
  [VECTO-695] - Bug in vectocmd.exe - process does not terminate
  [VECTO-699] - Output in manufacturer report and customer report (VECTO) uses different units than described in legislation
  [VECTO-700] - errorr in simulation with 0 stop time at the beginning of the cycle

## Slide 112: Vecto 3.2.1.1133 2018-02-07
Improvement
  [VECTO-634] - VTP Mode: specific fuel consumption
Bugfixes
  [VECTO-642] - VECTO BUG – secondary retarder losses: IMPORTANT: Fuel-consumption relevant bug! wrong calculation of retarder losses for retarder ratio not equal to 1
  [VECTO-624] - Crash w/o comment: Infinite recursion
  [VECTO-627] - Cannot open Engine-Only Job
  [VECTO-629] - Vecto crashes without errror message (same issue as VECTO-624)
  [VECTO-639] - Failed to find operating point for braking power: cycle with low target speed (3km/h). allow driving with slipping clutch
  [VECTO-640] - Exceeded max. iterations: driving fully-loaded vehicle steep uphill. fixed by allowing full-stop and drive off again
  [VECTO-633] - unable to start VTP Mode simulation
  [VECTO-645] - Encountered error while validating Vecto output (generated by API) through Hashing tool for vehicle without retarder

## Slide 113: Vecto 3.2.1.1079 2017-12-15
Improvement
  [VECTO-618] - Add Hash value of tyres to manufacturer's record file
  [VECTO-590] - Handling of hash values: customer's record contains hash of manufacturer's record
  [VECTO-612] - Continuously changing hashes: Info in GUI of HashingTool
  [VECTO-560] - Change Mail-Address of general VECTO contact
  [VECTO-616] - SI-Unit - display derived unit instead of base units
Bugfixes
  [VECTO-608] - Power balance in EPT-mode not closed
  [VECTO-611] - Invalid input. Cannot cast Newtonsoft.Json.Linq.JObject to Newtonsoft.Json.Linq.Jtoken
  [VECTO-610] - TyreCertificationNumber missing in Manufacturer Report
  [VECTO-613] - Incomplete description of allowed values of LegislativeClass (p251) in VECTO parameter documentation
  [VECTO-625] - Update XML Schema: Tyre dimensions according to Technicall Annex, trailing spaces in enums
Support
  [VECTO-615] - Error torque interpolation in declaration jobs exported to XMLImprovements

## Slide 114: Vecto 3.2.1.1054 2017-11-20
Improvements
[VECTO-592] - VTP Simulation Mode
[VECTO-605] - Improve simulation speed
Bugfixes
[VECTO-602] - Error in simulation without airdrag component
[VECTO-589] - Scheme .xml error

## Slide 115: VTP Simulation Mode
Verification Test Procedure (VTP) Simulation Mode
  Similar to Pwheel mode, different cycle format (see user manual)
  Requires:
    Vehicle in declaration mode (XML)
    Measured driving cycle
    Parameters for engine-fan model
  VECTO calculates the gear based on the wheel speed and engine speed (and vehicle parameters) and ignores the gear provided in the driving cycle
  Fuel consumption interpolation is done using the engine speed from the cycle and calculated power demand (to avoid wrong engine speeds due to wrong gear selection)
  Simulation uses all auxiliaries except engine fan
    Engine fan is modeled separately, power demand depends on fan speed (see user manual)
  Auxiliary power selected according to segment table, BUT power demand depends on vehicle speed
    v < 50 km/h: Urban
    50 <= v < 70 km/h: Rural
    v >70 km/h: Long haul
  Gear and fuel consumption in the driving cycle are optional for now, may be used in future versions

## Slide 116: Vecto 3.2.0.1022 2017-10-19
Bugfixes
[VECTO-585, VECTO-587] – VECTO Simulation aborts when run as WCF Service
[VECTO-586] – Gearshiftcout in reports too high
[VECTO-573] – Use of old library references .net framework 2.0

## Slide 117: Vecto 3.2.0.1005 2017-10-02
Improvements
Release of Vecto Hashing Tool
[VECTO-557] Engine speed simulated too high during long stops
Bugfixes
[VECTO-569] - ‘Engine Retarder’ not correctly recognized as input
[VECTO-571] - Customer Report – wrong output format of average RRC
[VECTO-573] - Correction of displayed units in graph window
[VECTO-575] - Correction of simulation aborts (due to gearbox inertia, engineering mode)
[VECTO-577] - Correction of XML export functionality
[VECTO-579] - Bug fix GUI crashes on invalid input
[VECTO-558] - Correction of output in .vsum file – BFColdHot always 0
[VECTO-564] - Bug fix: correct output of vehicle group in XML report
[VECTO-566] - Vehicle height not correctly read (engineering mode)
[VECTO-545] - Update documentation on Settings dialog

## Slide 118: Vecto 3.2.0.940 2017-07-28
Bugfixes
[VECTO-546] - GearboxCertificationOptionType Option 2 not accepted by VECTO
[VECTO-547] - Engine Manufacturer and Engine Model are empty in .vsum
[VECTO-548] - online user manual
[VECTO-549] - Inconsistent (and wrong) decimal separator in XML output (manufacturer report)
[VECTO-551] - Average Tyre RRC not in Customer Information File output
[VECTO-536] - GUI: improvements vehicle dialog (add missing pictures for vehicle categories)
[VECTO-550] - Allow custom settings for AirDensity in Engineering mode
[VECTO-552] - set engine rated power, rated speed to computed values from FLD if not provided as input

## Slide 119: Vecto 3.2.0.925 2017-07-14
Improvements
[VECTO-366] added EMS vehicle configuration, EMS is only simulated when engine rated power > 300kW
[VECTO-463] add pneumatic system technology 'vacuum pump‘
[VECTO-465] change RRC value of trailers (declaration mode) from 0.00555 to 0.0055 (due to limits in user interface)
[VECTO-477] AT Gearbox, powershift losses: remove inertia factor
[VECTO-471] update cross-wind correction model: height-dependent wind speed (see Excel spreadsheet in User Manual folder for details)
[VECTO-367] Add Vehicle Design Speed to segmentation table
[VECTO-470] Add XML reading and export functionality
[VECTO-486] Adding hashing library
[VECTO-469] Limit engine max torque (either due to vehicle or gearbox limits), limit gearbox input speed
[VECTO-466] Update vehicle payloads: 10% loaded and reference load are simulated
[VECTO-467] Add generic PTO activation in municipal cycle
[VECTO-468] Add PTO losses (idle) in declaration mode
[VECTO-479] Added PTO option 'only one engaged gearwheel above oil level' with 0 losses

## Slide 120: Vecto 3.2.0.925 2017-07-14
Improvements
[VECTO-483] Adapt CdxA supplement for additional trailers
[VECTO-494] Implementation of different fuel types
[VECTO-502] Implementing standard values for air-drag area (if not measured)
[VECTO-501] Implement engine idle speed set in vehicle (must be higher than engine's idle speed value)
[VECTO-504] Adding HVAC technology 'none‘
[VECTO-489] Extrapolate gearbox lossmaps (required when torque limitation by gearbox is ignored)
[VECTO-505] Implement AT transmissions in declaration mode
[VECTO-507] Allow to ignore validation of model data when starting a simulation (significant improvement on simulation startup time - about 10s)
[VECTO-506] modified method how torque-converter characteristics in drag is extended. allow drag-values in the input, only add one point at a high speed ratio
[VECTO-509] Add axle-type (vehicle driven, vehicle non-driven, trailer) to GUI
[VECTO-511] Add engine idle speed to Vehicle input form (GUI)
[VECTO-510] Write XML reports (manufacturer, customer information) in declaration mode
[VECTO-474] new driving cycles for Municipal and Regional Delivery

## Slide 121: Vecto 3.2.0.925 2017-07-14
Improvements
[VECTO-522] step-up ratio for using torque converter in second gear set to 1.85 for busses (still 1.8 for trucks)
[VECTO-525] remove info-box with max loading in GUI
[VECTO-531] Payload calculation: limit truck payload to the truck's max payload. (earlier versions only limited the total payload of truc + trailer to the total max. payload, i.e. allowed to shifted loading from truck to the trailer)
[VECTO-533] allow second driven axle, rdyn is calculated as average of both driven axles
[VECTO-537] new Suburban driving cycles
[VECTO-541] increase declaration mode PT1 curve to higher speeds (2500 is too low for some engines)
[VECTO-542] reduce overspeed in declaration mode to 2.5km/h

## Slide 122: Vecto 3.2.0.925 2017-07-14
Bugfixes
[VECTO-462] fix: decision if PTO cycle is simulated
[VECTO-473] fix: adapt range for validation of torque converter characteristics
[VECTO-464] fix: extrapolation of engine full-load curve gives neg. max. torque. Limit engine speed to n95h
[VECTO-480] fix: a_pos in .vsum was less than zero
[VECTO-487] fix: Duration of PTO cycle was computed incorrectly if PTO cycle does not start at t=0
[VECTO-514] fix: sort entries in .vsum numerically, not lexically
[VECTO-516] fix: consider axlegear losses for estimation of acceleration after gearshifts
[VECTO-517] fix: valid shift polygon was considered invalid when extended to very high torque ranges
[VECTO-424] fix: VectoCore.dll could not be found when the current working directory is different to the directory of the vectocmd.exe
[VECTO-425] fix: vectocmd.exe - check if the output is redirected, and skip updating of the progress bar when this is the case
[VECTO-426] fix: vectocmd.exe - log errors to STDERR
[VECTO-519] fix: computation of n95h fails for a valid full-load curve due to numerical inaccuracy. add tolerance when searching for solutions
[VECTO-520] fix: gearashift count in vsum is 0

## Slide 123: Vecto 3.1.2.810 2017-01-18
Improvements
[VECTO-445] Additional columns in vsum file
Allow splitting shift losses among multiple simulation intervals
Allow coasting overspeed only if vehicle speed > 0
Torque converter: better handling of ‘creeping’ situations
Bugfixes:
[VECTO-443] Bugfix in AMT shift strategy: skip gears not working correctly

## Slide 124: Vecto 3.1.2.796 2017-03-07
Improvements:
[VECTO-405] Adding clutch-losses for AMT/MT gearboxes during drive-off, reduce drive-off distance after stop from 1m to 0.25m, set clutch closing speed (normalized) to 6.5%, changes in clutch model
[VECTO-379] Make GUI more tolerant against missing files. Instead of aborting reading the input data the GUI shows a suffix for missing input files
[VECTO-411] Allow a traction interruption of 0s for AMT/MT gearboxes
[VECTO-408] Gearbox Inertia for AT gearboxes set to 0
[VECTO-419] Adapted error messages, added list of errors
[VECTO-421,VECTO-439] Added volume-related results to vsum file (volume is computed based on default bodies)
[] Energy balance (vsum) and balance of engine power output and power consumers (vmod) level
[VECTO-430] AT shift strategy: upshifts may happen too early
[VECTO-431] AMT shift strategy always started in first gear due to changes in clutch model
[VECTO-433] adapt generic vehicles: use typical WHTC correction factors
[VECTO-437] set vehicle speed at clutch-closed to 1.3 m/s
[VECTO-436] fix simulation aborts with AT gearbox (neg. braking power, unexpected response, underload)
Bugfixes:
[VECTO-415] Powershift Losses were not considered for AT gearboxes with PowerSplit
[VECTO-416] Measured Speed with gear failed when cycle contained parts with eco-roll (computation of next gear failed)
[VECTO-428] Sum of timeshares adds up to 100%
[VECTO-429] Min Velocity for lookahead coasting was not written to JSON file

## Slide 125: Vecto 3.1.1.748 2017-01-18
Bugfixes:
[VECTO-404] Driving Cycle with PTO stopped simulation after first PTO activation

## Slide 126: Vecto 3.1.1.742 2017-01-12
Improvements:
[VECTO-390, VECTO-400] Adapt engine speed to estimated engine speed after gear shift during traction interruption (double clutching)
[VECTO-396, VECTO-388] Add shift losses for AT power shifts
[VECTO-389] new gear shift rules for AT gearboxes
[VECTO-387] added max input speed for torque converter
[VECTO-385] Automatically add generic torque converter data for drag
[VECTO-399] Add missions and loadings for vehicle categories 11, 12, and 16 (declaration mode)
[VECTO-384] cleanup memory after simulation run
[VECTO-394] new option for vectocmd to disable all output
[VECTO-392] make the GUI scale depending on the Windows font size
[VECTO-391] Gearbox output speed and output torque added to .vmod files
[VECTO-386] Gearbox window: disable input fields not applicable for the selected gearbox type
Bugfixes:
[VECTO-401] Computation of n_95h etc. fails if engine’s max torque is constant 0
Lookup of Airdrag parameters in declaration mode
[VECTO-378] Improved file-handling in AAUX module

## Slide 127: Vecto 3.1.0.683 2016-11-14
Bugfixes:
[VECTO-375] Fixed bug when braking during slope change from negative to positive values.
[VECTO-372] Added check for unusual acceleration/deceleration data which could lead to error when halting.
[VECTO-371] Added additional behavior to overcome such situations
[VECTO-370] Added additional behavior to overcome such situations
[VECTO-369] CrosswindCorrection is now saved and read again from JSON files
[VECTO-373] WHTC-Engineering correction factor now correctly read/write in JSON files
[VECTO-368] Fixed validation for specific cases when values are intentionally invalid.
[VECTO-357] Updated GUI to not show ECO-Roll option to avoid confusion
Fixed numerous bugs in AT-ShiftStrategy regarding the Torque Converter
Fixed numerous bugs in MeasuredSpeed Mode (and MeasuredSpeed with Gear) in connection with AT-Gearbox and TorqueConverter
Fixed a bug when PTO-Cycle was missing
Corrected axle loss maps for Generic Vehicles in Declaration Mode to match technical annex
Corrected SumFile Cruise Time Share. Added that timeshares must add up to 100%

## Slide 128
Improvements:
[VECTO-355] Updated documentation, added powertrain schematics in chapter "Simulation Models"
[VECTO-374] Check range for Torque Converter speed ratio input data to be at least between 0 and 2.2
Updated many error messages to be more explicit about the reason of error
Added "Mission Profiles" Directory with driving cycles publicly available in the application root directory.
Added "Declaration" directory with the declaration data files in the application root directory.
Added warning when engine inertia is 0
Added check that engine speed must not fall below idle speed (even in measured speed mode)
Shift curve validation for AT gearboxes: shift curves may now overlap due to different shift logic in AutomaticTransmissions.
Updated Crosswind Coefficients for Tractor+Semitrailer
Vecto 3.1.0.683 2016-11-14

## Slide 129: Vecto 3.1.0.662 2016-10-24
Bugfixes:
  [VECTO-360] Fixed error during startup of VECTO (loading of DLLs).
  [VECTO-358] Fixed errors during simulation where vehicle unintentionally was driving backwards. Fixed 1Hz-Filter for ModFiles (distance was wrong under certain circumstances, vehicle seemingly jumping back before halt)
  [VECTO-361] Fixed classification of vehicles with GVM of exactly 7500kg
  [VECTO-364] Fixed an error in measured speed mode (run aborts).
  [VECTO-363] Compute shift polygons in declaration mode now uses correct boundary for full load margin.
  [VECTO-365] Fixed editing gears in declaration mode
Improvements:
  [VECTO-355] User Manual updated (Screenshots, Descriptions, File Formats, Vecto V2 Comments removed).
  [VECTO-317] Declaration data for Wheel sizes updated
  [VECTO-359] Simplified code regarding PT1 behavior.
  [VECTO-323] PTO-Cycle may now be left empty when not used in driving cycle.

## Slide 130: Vecto 3.1.0.652 2016-10-14
Main Updates
  Removed VECTO Core 2.2
  Refactoring of the User-Interface Backend: loading, saving files and validating user input uses Vecto 3 models
  AT-Gearbox Model: differentiate between AT gearbox with serial torque converter and AT gearbox using powersplit
  Numbering of gears with AT gearbox corresponds to mechanical gears, new column TC_locked in .vmod file to indicate if torque converter is active
  Torque converter gear no longer allowed in input (added by Vecto depending on the AT model)
  New implementation of torque converter model (analytic solutions)
  Added PTO option for municipal utility vehicles: PTO idle losses, separate PTO cycle during standstill
  Added Angledrive Component
  Option for constant Auxiliary Power Demand in Job-File

## Slide 131: Vecto 3.1.0.652 2016-10-14
Main Updates (cont.)
  Normalize x/y values before triangulating Delaunay map (transmission loss-maps, fuel consumption loss map)
  Additional fuel consumption correction factor in declaration mode: cold/hot balancing factor
  Added fuel consumption correction factor (WHTC, Cold/Hot balancing, …) in engineering mode
  Update auxiliaries power demand according to latest whitebook
  Allow multiple steered axles
  Adapted engine idle controller (during declutch) – engine speed decreases faster
  SUM-File: split E_axl_gbx into two columns, E_axl and E_gbx
  New columns in mod-file: PTO, torque converter
  Removed full-load curve per gear, only single value MaxTorque
  Removed rims (dynamic wheel radius depends on wheel type)
  Fixes in AAUX module: open correct file-browser, save selected files

## Slide 132: Status quo VECTO software and open issues (Oct. 2016)
Next issues on the to do list
Further development of the AT model Consideration of losses during power shifts, update of gear shift logics
Reimplementation of engine stop/start
Declaration mode: implementation of EMS vehicle configurations
Items waiting for decision on methods and resources:
Update engine data (according to update of Annex II) Other fuels than diesel, “top torque” feature, correction factor for periodic regerating DPFs
Declaration mode:
  Revision of calculated vehicle loads
  implementation of refuse cycle (instead “municipal”) Update of driving cycle, consideration of generic PTO loads during collection part, generic body weight and payload
  VECTO output (approval authorities, customer info, monitoring)
  Buses
Predictive ADAS

## Slide 133: Vecto 3.0.4.565 2016-07-19
Bugfixes
  AAUX HVAC Dialog does not store path to ActuationsMap and SSMSource
  GUI: check for axle loads in declaration mode renders editing dialog useless
  Vecto 2.2: Simulation aborts (Vecto terminates) when simulating EngineOnly cycles
  Vecto 3: Building SimulationRun EngineOnly simulation failed

## Slide 134: Vecto 3.0.4.544 2016-06-28
Main Updates
  New gear shift strategy according to White Book 2016
  New coasting strategy according to White Book 2016
  New input parameters (enineering mode) for coasting and gear shift behavior
  Use SI units in Advanced Auxiliaries Module and compile with strict compiler settings (no implicit casts, etc.)
  Allow efficiency for transmission losses (in engineering mode)
Bugfixes
  Auxiliary TechList not read from JSON input data
  Improvements in driver strategy
  Bugfixes in MeasuredSpeed mode

## Slide 135: Notes for using Vecto 3.x with AAUX (1)
The AdvancedAuxiliaries module requires the number of activations for pneumatic consumers (brakes, doors, kneeling) and the (estimated) total cycle time. This can be configured in the .APAC-file (actuations file). For standard bus/coach cycles (i.e., the cycle file contains “bus” and “heavy_urban” or “suburban” or “interurban” or “urban”; or the cycle contains “coach” (case insensitive)) the actuations file already contains the number of activations and the cycle time. For other cycles the filename without extension is used to lookup the activations in the .APAC file (case sensitive)

## Slide 136: Notes for using Vecto 3.x with AAUX (2)
Vecto 3 uses an average auxiliaries load (determined by the AAUX module depending on the settings) for the simulation. The AAUX module computes the fuel consumption in parallel to VectoCore and accounts for smart consumers (e.g., alternator, pneumatics, …).
Output
  The .vmod file contains both, the fuel consumption calculated by VectoCore (per simulation interval) and AAUX (accumulated and per simulation interval). Columns in .vmod file:
    AA_TotalCycleFC_Grams [g]: accumulated fuel consumption as computed by the AAUX model, considering smart consumers
    FC-Map [g/h]: fuel consumption as computed by VectoCore interpolating in the FC-Map, using an average base load of auxiliaries
    FC-AUXc [g/h]: fuel consumption corrected due to engine stop/start (currently not applicable)
    FC-WHTCc [g/h]: WHTC-corrected fuel consumption (not applicable in engineering mode)
    FC-AAUX [g/h]: fuel consumption per simulation interval, derived from AA_TotalCycleFC_Grams
    FC-Final [g/h]: final fuel consumption value with all (applicable) corrections applied (stop/start, WHTC, smart auxiliaries)

## Slide 137: Notes for using Vecto 3.x with AAUX (3)
Output .vsum
  Columns in .vsum file:
    FC-Map: total fuel consumption as computed by VectoCore interpolating in the FC-Map, using an average base load of auxiliaries
    FC-AUXc: total fuel consumption corrected due to engine stop/start (currently not applicable)
    FC-WHTCc: WHTC-corrected fuel consumption (not applicable in engineering mode)
    FC-AAUX: fuel consumption per simulation interval, derived from AA_TotalCycleFC_Grams
    FC-Final: final fuel consumption value with all (applicable) corrections applied (stop/start, WHTC, smart auxiliaries)

## Slide 138: Vecto 3.0.3.537 2016-06-21
Main Updates
  Plot shift lines as computed according to WB 2016 declaration mode in GUI
Bugfixes
  GUI: Buttons to add/remove auxiliaries are visible again
  Error in calculation of WHTC correction factor
  Fix: consider gearbox inertia (engineering mode) for searching operating point
  Wrong output of road gradient in measured speed mode (correct gradient for simulation)
  Fuel consumption in .vsum file now accounts for AdvancedAuxiliaries model
  GraphDrawer (Vecto): handle new .vmod format of Vecto 3
  AdvancedAuxiliaries: language-settings independent input parsing
  Paux was ignored when running Vecto 2.2
  Error in massive multithreaded execution
  Fix unhandled response during simulation
  Fix output columns in .vmod

## Slide 139: Vecto 3.0.3.495 2016-05-10
Main Updates
  Support for Advanced Auxiliaries (Ricardo) in Vecto 3.0.3 and Vecto 2.2
  Performance improvements
  Gearshift polygons according to WB 2016
  Revision of SUM-data file, changed order of columns, changed column headers
Bugfixes
  Delaunay Maps: additional check for duplicate input points
  Creation of PDF Report when running multiple jobs at once
  Sanity checks for gear shift lines
  Improvements DriverStrategy: handling special cases

## Slide 140: Performance Comparison
Time [s]
Total execution time (15 runs in parallel): Vecto 3.0.2: 6min 6s; Vecto 3.0.3: 35s

## Slide 141
VECTO 3.0.2 2016-03-11
Main updates
New simulation modes:
  Pwheel (SiCo),
  Measured Speed (with/without gear)
  v_air/beta cross-wind correction (vcdb)
Adaptations of powertrain components architecture
  Move wheels inertia from vehicle to wheels
  Auxiliaries no longer connected via clutch to the engine but via a separate port
  Engine checks overload of gearbox and engine overload
Fixed some driving behavior related issues in VectoCore:
  When the vehicle comes to a halt during gear shift, instead of aborting the cycle, it tries to drive away again with an appropriate gear.
ModData Format changed for better information and clarity
Added validation of input values (according to latest VectoInputParameters.xls)
Various bugfixes

## Slide 142: Pwheel (SiCo) Mode
Function as already available in Vecto 2.2 also added in Vecto 3.0.2
  Driving cycle specifies power at wheel, engine speed, gear, and auxiliary power
  No driver model in the simulation.
  The Vecto gear-shift model is overruled.
  Function used for creating reference results for SiCo tests
  For details see user manual: Simulation Models / Pwheel Input (SiCo)

## Slide 143: Measured Speed Mode
Functionality already available in Vecto 2.2 added in Vecto 3.0.2
  Driving cycle not defined by target speed but by actual speed. No driver model in the simulation.
  Gear and engine speed can be specified in the driving cycle. In this case the Vecto gear-shift model is overruled.
  Function used for “proof of concept” purposes
  For details see user manual: Calculation Modes / Engineering Mode / Measured Speed

## Slide 144: .vmod File Update
In Vecto 3.0.2 the structure of the modal data output has been revised and re-structured. Basicaly for every powertrain component the .vmod file contains the power at the input shaft and the individual power losses for every component. For the engine the power, torque and engine speed at the output shaft is given along with the internal power and torque used for computing the fuel consumption.
For details see the user manual: Input and Output / Modal Results (.vmod)

## Slide 145: Changelog 3.0.2
- New simulation modes:
+ Measured Speed
+ Measured Speed with Gear
+ Pwheel (SiCo)
- Adaptations of powertrain components architecture
+ Move wheels inertia from vehicle to wheels
+ Auxiliaries no longer connected via clutch to the engine but via a separate port
+ Engine checks overload of gearbox and engine overload
- Fixed some driving behavior related issues in VectoCore:
+ When the vehicle comes to a halt during gear shift, instead of aborting the cycle, it tries to drive away again with an appropriate gear.
- [ModData Format](#modal-results-.vmod) changed for better information and clarity
- Entries in the sum-file are sorted in the same way as in Vecto 2.2
- In engineering mode the execution mode (distance-based, time-based measured speed, time-based measured speed with gear, engine only) are detected based on the cycle
- Added validation of input values
- Gravity constant set to 9.80665 (NIST standard acceleration for gravity)
- Improved input data handling: sort input values of full-load curves (engine, gbx, retarder)
- Better Integration of VectoCore into GUI (Notifications and Messages)
- v_air/beta cross-wind correction (vcdb) impemented
- For all calculations the averaged values of the current simulation step are used for interpolations in loss-maps.
- Allow extrapolation of loss maps in engineering mode (warnings)
- Refactoring of input data handling: separate InputDataProvider interfaces for model data
- Refactoring of result handling: separate result container and output writer
- New Long-Haul driving cycle included
- User Manual updated for VECTO V3.x
- Fix: sparse representation of declaration cycles had some missing entries
- Bugfix: error in computation of engine's preferred speed
- Bugfix: wrong vehicle class lookup
- Bugfix: duplicate entries in intersected full-load curves
- Bugfix: retarder takes the retarder ratio into account for lossmap lookup
- Bugfix: use unique identifier for jobs in job list
- Bugfix: error in triagulation of fuel consumption map