## Slide 1
VECTO 3.x 14.10.2016
Release Notes

## Slide 2: Vecto 3.1.0.652
Main Updates
  Removed VECTO Core 2.2
  Refactoring of the User-Interface Backend: loading, saving files and validating user input uses Vecto 3 models
  AT-Gearbox Model: differentiate between AT gearbox with serial torque converter and AT gearbox using powersplit
  Numbering of gears with AT gearbox corresponds to mechanical gears, new column TC_locked in .vmod file to indicate if torque converter is active
  Torque converter gear no longer allowed in input (added by Vecto depending on the AT model)
  New implementation of torque converter model (analytic solutions)
  Added PTO option for municipal utility vehicles: PTO idle losses, separate PTO cycle during standstill
  Added Angledrive Component
  Option for constant Auxiliary Power Demand in Job-File

## Slide 3: Vecto 3.1.0.652
Main Updates (cont.)
  Normalize x/y values before triangulating Delaunay map (transmission loss-maps, fuel consumption loss map)
  Additional fuel consumption correction factor in declaration mode: cold/hot balancing factor
  Added fuel consumption correction factor (WHTC, Cold/Hot balancing, …) in engineering mode
  Update auxiliaries power demand according to latest whitebook
  Allow multiple steered axles
  Adapted engine idle controller (during declutch) – engine speed decreases faster
  SUM-File: split E_axl_gbx into two columns, E_axl and E_gbx
  New columns in mod-file: PTO, torque converter
  Removed full-load curve per gear, only single value MaxTorque
  Removed rims (dynamic wheel radius depends on wheel type)
  Fixes in AAUX module: open correct file-browser, save selected files

## Slide 4: Status quo VECTO software and open issues (Oct. 2016)
Next issues on the to do list
Further development of the AT model Consideration of losses during power shifts, update of gear shift logics
Reimplementation of engine stop/start
Declaration mode: implementation of EMS vehicle configurations
Items waiting for decision on methods and resources:
Update engine data (according to update of Annex II) Other fuels than diesel, “top torque” feature, correction factor for periodic regerating DPFs
Declaration mode:
  Revision of calculated vehicle loads
  implementation of refuse cycle (instead “municipal”) Update of driving cycle, consideration of generic PTO loads during collection part, generic body weight and payload
  VECTO output (approval authorities, customer info, monitoring)
  Buses
Predictive ADAS

## Slide 5: Vecto 3.0.4.565
Bugfixes
  AAUX HVAC Dialog does not store path to ActuationsMap and SSMSource
  GUI: check for axle loads in declaration mode renders editing dialog useless
  Vecto 2.2: Simulation aborts (Vecto terminates) when simulating EngineOnly cycles
  Vecto 3: Building SimulationRun EngineOnly simulation failed

## Slide 6: Vecto 3.0.4.544
Main Updates
  New gear shift strategy according to White Book 2016
  New coasting strategy according to White Book 2016
  New input parameters (enineering mode) for coasting and gear shift behavior
  Use SI units in Advanced Auxiliaries Module and compile with strict compiler settings (no implicit casts, etc.)
  Allow efficiency for transmission losses (in engineering mode)
Bugfixes
  Auxiliary TechList not read from JSON input data
  Improvements in driver strategy
  Bugfixes in MeasuredSpeed mode

## Slide 7: Notes for using Vecto 3.x with AAUX (1)
The AdvancedAuxiliaries module requires the number of activations for pneumatic consumers (brakes, doors, kneeling) and the (estimated) total cycle time. This can be configured in the .APAC-file (actuations file). For standard bus/coach cycles (i.e., the cycle file contains “bus” and “heavy_urban” or “suburban” or “interurban” or “urban”; or the cycle contains “coach” (case insensitive)) the actuations file already contains the number of activations and the cycle time. For other cycles the filename without extension is used to lookup the activations in the .APAC file (case sensitive)

## Slide 8: Notes for using Vecto 3.x with AAUX (2)
Vecto 3 uses an average auxiliaries load (determined by the AAUX module depending on the settings) for the simulation. The AAUX module computes the fuel consumption in parallel to VectoCore and accounts for smart consumers (e.g., alternator, pneumatics, …).
Output
  The .vmod file contains both, the fuel consumption calculated by VectoCore (per simulation interval) and AAUX (accumulated and per simulation interval). Columns in .vmod file:
    AA_TotalCycleFC_Grams [g]: accumulated fuel consumption as computed by the AAUX model, considering smart consumers
    FC-Map [g/h]: fuel consumption as computed by VectoCore interpolating in the FC-Map, using an average base load of auxiliaries
    FC-AUXc [g/h]: fuel consumption corrected due to engine stop/start (currently not applicable)
    FC-WHTCc [g/h]: WHTC-corrected fuel consumption (not applicable in engineering mode)
    FC-AAUX [g/h]: fuel consumption per simulation interval, derived from AA_TotalCycleFC_Grams
    FC-Final [g/h]: final fuel consumption value with all (applicable) corrections applied (stop/start, WHTC, smart auxiliaries)

## Slide 9: Notes for using Vecto 3.x with AAUX (3)
Output .vsum
  Columns in .vsum file:
    FC-Map: total fuel consumption as computed by VectoCore interpolating in the FC-Map, using an average base load of auxiliaries
    FC-AUXc: total fuel consumption corrected due to engine stop/start (currently not applicable)
    FC-WHTCc: WHTC-corrected fuel consumption (not applicable in engineering mode)
    FC-AAUX: fuel consumption per simulation interval, derived from AA_TotalCycleFC_Grams
    FC-Final: final fuel consumption value with all (applicable) corrections applied (stop/start, WHTC, smart auxiliaries)

## Slide 10: Vecto 3.0.3.537
Main Updates
  Plot shift lines as computed according to WB 2016 declaration mode in GUI
Bugfixes
  GUI: Buttons to add/remove auxiliaries are visible again
  Error in calculation of WHTC correction factor
  Fix: consider gearbox inertia (engineering mode) for searching operating point
  Wrong output of road gradient in measured speed mode (correct gradient for simulation)
  Fuel consumption in .vsum file now accounts for AdvancedAuxiliaries model
  GraphDrawer (Vecto): handle new .vmod format of Vecto 3
  AdvancedAuxiliaries: language-settings independent input parsing
  Paux was ignored when running Vecto 2.2
  Error in massive multithreaded execution
  Fix unhandled response during simulation
  Fix output columns in .vmod

## Slide 11: Vecto 3.0.3
Main Updates
  Support for Advanced Auxiliaries (Ricardo) in Vecto 3.0.3 and Vecto 2.2
  Performance improvements
  Gearshift polygons according to WB 2016
  Revision of SUM-data file, changed order of columns, changed column headers
Bugfixes
  Delaunay Maps: additional check for duplicate input points
  Creation of PDF Report when running multiple jobs at once
  Sanity checks for gear shift lines
  Improvements DriverStrategy: handling special cases

## Slide 12: Performance Comparison
Time [s]
Total execution time (15 runs in parallel): Vecto 3.0.2: 6min 6s; Vecto 3.0.3: 35s

## Slide 13
VECTO 3.0.2
Main updates
New simulation modes:
  Pwheel (SiCo),
  Measured Speed (with/without gear)
  v_air/beta cross-wind correction (vcdb)
Adaptations of powertrain components architecture
  Move wheels inertia from vehicle to wheels
  Auxiliaries no longer connected via clutch to the engine but via a separate port
  Engine checks overload of gearbox and engine overload
Fixed some driving behavior related issues in VectoCore:
  When the vehicle comes to a halt during gear shift, instead of aborting the cycle, it tries to drive away again with an appropriate gear.
ModData Format changed for better information and clarity
Added validation of input values (according to latest VectoInputParameters.xls)
Various bugfixes

## Slide 14: Pwheel (SiCo) Mode
Function as already available in Vecto 2.2 also added in Vecto 3.0.2
  Driving cycle specifies power at wheel, engine speed, gear, and auxiliary power
  No driver model in the simulation.
  The Vecto gear-shift model is overruled.
  Function used for creating reference results for SiCo tests
  For details see user manual: Simulation Models / Pwheel Input (SiCo)

## Slide 15: Measured Speed Mode
Functionality already available in Vecto 2.2 added in Vecto 3.0.2
  Driving cycle not defined by target speed but by actual speed. No driver model in the simulation.
  Gear and engine speed can be specified in the driving cycle. In this case the Vecto gear-shift model is overruled.
  Function used for “proof of concept” purposes
  For details see user manual: Calculation Modes / Engineering Mode / Measured Speed

## Slide 16: .vmod File Update
In Vecto 3.0.2 the structure of the modal data output has been revised and re-structured. Basicaly for every powertrain component the .vmod file contains the power at the input shaft and the individual power losses for every component. For the engine the power, torque and engine speed at the output shaft is given along with the internal power and torque used for computing the fuel consumption.
For details see the user manual: Input and Output / Modal Results (.vmod)

## Slide 17: Changelog 3.0.2
- New simulation modes:
+ Measured Speed
+ Measured Speed with Gear
+ Pwheel (SiCo)
- Adaptations of powertrain components architecture
+ Move wheels inertia from vehicle to wheels
+ Auxiliaries no longer connected via clutch to the engine but via a separate port
+ Engine checks overload of gearbox and engine overload
- Fixed some driving behavior related issues in VectoCore:
+ When the vehicle comes to a halt during gear shift, instead of aborting the cycle, it tries to drive away again with an appropriate gear.
- [ModData Format](#modal-results-.vmod) changed for better information and clarity
- Entries in the sum-file are sorted in the same way as in Vecto 2.2
- In engineering mode the execution mode (distance-based, time-based measured speed, time-based measured speed with gear, engine only) are detected based on the cycle
- Added validation of input values
- Gravity constant set to 9.80665 (NIST standard acceleration for gravity)
- Improved input data handling: sort input values of full-load curves (engine, gbx, retarder)
- Better Integration of VectoCore into GUI (Notifications and Messages)
- v_air/beta cross-wind correction (vcdb) impemented
- For all calculations the averaged values of the current simulation step are used for interpolations in loss-maps.
- Allow extrapolation of loss maps in engineering mode (warnings)
- Refactoring of input data handling: separate InputDataProvider interfaces for model data
- Refactoring of result handling: separate result container and output writer
- New Long-Haul driving cycle included
- User Manual updated for VECTO V3.x
- Fix: sparse representation of declaration cycles had some missing entries
- Bugfix: error in computation of engine's preferred speed
- Bugfix: wrong vehicle class lookup
- Bugfix: duplicate entries in intersected full-load curves
- Bugfix: retarder takes the retarder ratio into account for lossmap lookup
- Bugfix: use unique identifier for jobs in job list
- Bugfix: error in triagulation of fuel consumption map